## Slide 1: Presented At: The 40th Eastern VHF / UHF Conference By: Fred Stefanik, N1DPM
A Fresh Approach To A Multi-Band Microwave Station
Notes: <number>

## Slide 2: A Fresh Approach To A Multi-Band Microwave Station
1984 (that’s right 30 years ago!)(I was 23 years old)
  I first tried 1296 out at my home QTH at FN32qb.
    500mW transverter (Borrowed from WB1FVS)
    13 element Yagi (Borrowed from K1FO)
    100 feet of RG8U Feedline
    I worked….
      W2SZ/1 @ ~ 50 miles
      W1JR @ ~ 73 miles
  The microwave bug bit!
1988
  1296 Gear of my own now!
    SSB LT23S
    45 Element Loop Yagi
    100 Feet of 3/4” *OLD* CATV Aluminum Hardline
      Of Unknown Quality
    Could now work about 6 or 7 stations!

## Slide 3: A Fresh Approach To A Multi-Band Microwave Station
1990
  Moved the LT23S to a weatherproof box up on the tower.
    Now I had my 10 watts near the antenna
    I also had my receiver front end there too
    I saw a marked increase in overall performance
The microwave bug bit again!
  Over the next few years I added more bands…
  All Transverters, etc up on the tower.
    903
      10 watts, 3dB NF,Loop Yagi
    2304
      1 watt, 2dB NF, Loop Yagi
    3456
      1 watt, 2dB NF, Loop Yagi
  This stuff worked really good at the antenna!

## Slide 4: A Fresh Approach To A Multi-Band Microwave Station
~ 1997
  Time to rebuild the antennas and systems on the tower.
    The original LT23S had died
      It was time for a new 1296 system too.
  The New Tower Mounted Systems Were…
    903 - 70 Watts, 0.7dBNF, 39 element 15’ Boom Looper
    1296 - 35 Watts, 0.3dBNF, 55 element 15’ Boom Looper
    2304 - 40 Watts, 1dBNF, 76 element 12’ Boom Blowtorch
    3456 - 10 Watts, 1dBNF, 112 element 12’ Boom Blowtorch
      All feedlines on these systems were ~10’ of FSJ4-50B Superflex
    I also added….
    5760 - 2 Watts DEMI Transverter, 2’ Dish
    10368 - 3 Watts, Kuhne Transverter, DL2AM amplifier, 2’ Dish
      ~2003 I added a DEMI 8 Watt amp to the 10GHz system.
  This stuff worked great!
  Time marches on…..

## Slide 5: A Fresh Approach To A Multi-Band Microwave Station
  903 MHz
    17.9dBd Antenna Gain
    0.35dB Feedline Loss
    3,982 Watts ERP
    1.05dB System NF
  2304 MHz
    21.3dBd Antenna Gain
    0.58dB Feedline Loss
    4,721 Watts ERP
    1.58dB System NF
  1296 MHz
    18.9dBd Antenna Gain
    0.41dB Feedline Loss
    2,472 Watts ERP
    0.71dB System NF
  3456 MHz
    23.1dBd Antenna Gain
    0.74dB Feedline Loss
    1,722 Watts ERP
    1.74dB System NF
Performance of this gear looks like...

## Slide 7: A Fresh Approach To A Multi-Band Microwave Station
2013
  It’s now 29 years after my first endeavor on 1296.
  It’s been ~ 16 years since my antenna system was last overhauled.
  I’m now 52 not 23
    I know I’m young still, but….
  I decided I wanted a really good system on this tower for….
    6 Meters, 2 Meters, 222MHz, and 432MHz
  So I ask my friend John AA1I/R if he could help me as ground crew to do some tower work.
  The first day we took down 903, 1296, and 2304.
    After wrenching apart 16 year old hardware on these 3 systems I was shot!
    More next time….
  A week later when he arrived he said “let me go up and give it a shot”
    OOOOHHHHH….A younger guy to help on the tower!
    We took down the 2 meter yagis, 3456, 5760, and 10GHz.
    This time the “youngster” was shot!

## Slide 8: A Fresh Approach To A Multi-Band Microwave Station
2013 continued….
  After his first time on the tower he said something like….
    You got me into this microwave stuff and here I am helping you take apart one of the stations I can reliably work as a rover. Something seems wrong with that!
  Well that had some influence….
  He bought all his own climbing harness, etc and continued to help with the antenna system rebuild.
  I continued to play ground crew!

## Slide 11: A Fresh Approach To A Multi-Band Microwave Station
OK….6 Meters through 432 were up and working
I started to think about how I may approach the lower 4 microwave bands.
My old 6 bands worth of gear found a new home in FN43cd
I looked at what I had kicking around
And…
Thought about how I could get on with the goals of…
  Getting on easily
    Keep the set up simple
  Easy maintenance on the tower (I’m not getting any younger)
  “Reasonable Performance”
    I want to be able to work AA1I/R where he goes
    I’d like to work out to the ~100 mile radius or so

## Slide 12: A Fresh Approach To A Multi-Band Microwave Station
Antennas….small
  This is a portable array I only used a few times.
  5’ Fiberglass cross boom
903
  Commercial 13 element yagi spec’d at 13dBd gain
1296
  Homebrew DL6WU 14 element yagi - 14.2dBd gain
2304
  W1RIL 22 element looper ~ 17.5 dBd gain
3456
  Directive Systems 22 element looper ~ 17.5 dBd gain
Remove the horn antenna and now I have a place for a LNA

## Slide 13: A Fresh Approach To A Multi-Band Microwave Station
Goals:
  Simple
  Bands = 902/3, 1296, 2304, 3456
  Transverters and PA’s in shack
  LNA on Tower for good RX performance
  One 100’ piece of LDF4-50 Heliax Feedline
    903 Loss = 2.2dB
    1296 Loss = 2.7dB
    2304 Loss = 3.8dB
    3456 Loss = 4.6dB
  Decent Performance

## Slide 14: A Fresh Approach To A Multi-Band Microwave Station
LNA
  Switching multiple LNA’s too complex
  Good performance broadband LNA
    AD6IW HEMT MMIC LNA from NEWS site
      Contacted Goran and told him what I was looking for
      He made an LNA for me
      It tested to the following specs…
        903 - 24.4dB Gain - 0.31dB Noise Figure
        1296 - 22.7dB Gain - 0.30dB Noise Figure
        2304 - 17.8dB Gain - 0.48dB Noise Figure
        3456 - 14.9dB Gain - 0.56dB Noise Figure

## Slide 15: A Fresh Approach To A Multi-Band Microwave Station
LDF4-50
Common
Feed Line
LNA
LNA
Bypass
Relay
4 Position
Antenna
Selector
Relay
903 1.2 2.3 3.4

## Slide 16: A Fresh Approach To A Multi-Band Microwave Station

## Slide 17: A Fresh Approach To A Multi-Band Microwave Station
903 - 13 Element
Cushcraft Commercial
Yagi
3456 - 22 Element
Directive Systems
Looper
1296 - 14 Element
Home Brew DL6WU
Yagi
2304 - 22 Element
W1RIL Loop Yagi

## Slide 19: A Fresh Approach To A Multi-Band Microwave Station
The LNA works great!
It has a high P-1dB and OIP3
  +23dBm P-1dB
  +40dBm OIP3
  So it won’t overload….but…
  What about the Transverters?
  YES THEY DO!!!!
902.600 MHz Center Frequency
10 dB/ Div 10 MHz / Div
0 dBm Top Reference!

## Slide 20: A Fresh Approach To A Multi-Band Microwave Station
Now turn on the peak hold function on the spectrum analyzer and let it run a while….
Same settings as before
There are peaks at -10dBm!
You can also see the result of the frequency agile signal that moves from ~902 to ~925 MHz that is -30dBm.
S9 on my receiver = -100dBm
This out of band interference is S9 + 90dB!
The in band interference is S9 + 70dB!
  Good thing the in band hops around!
Bottom picture is 2 MHz / Div
Looks like I need a filter!

## Slide 21: A Fresh Approach To A Multi-Band Microwave Station
Here’s a picture taken with the 902 / 903 receive filter in place.
This is more tolerable but still not great.
Top Picture 10 MHz / Div
Bottom Picture 2 MHz / Div

## Slide 22: A Fresh Approach To A Multi-Band Microwave Station
Without
Filter
With
Filter

## Slide 23: A Fresh Approach To A Multi-Band Microwave Station
These are the other bands
  1296 Could use a filter
    Seems to hear OK now
  2304 Could use a filter
    Seems to hear OK now
  3456 Is clean as is
These pictures are taken at
  1296 MHz Center
  2304 MHz Center
  3456 MHz Center
  0 dBm reference
  10dB / Division
  100 MHz / Division

## Slide 24: A Fresh Approach To A Multi-Band Microwave Station

## Slide 25: A Fresh Approach To A Multi-Band Microwave Station

## Slide 26: A Fresh Approach To A Multi-Band Microwave Station
Microwave Station:
  IF
    TS850S ->Down East Microwave 28-144 Transverter
  903
    Down East Microwave 902/3-144 Transverter
    Freescale MRFE6VP8600H LDMOS Amplifier
      300+ Watts
  1296
    Down East Microwave 1296-144
    Infineon PTF141501 LDMOS Amplifier
      150 Watts (I have 250 watt amplifier, I just need to hook it up!)
  2304
    SHF Systems 2304-144
    Surplus MMDS amplifiers
      8 Watts
      LDMOS amp in the works for ~250 W (NXP BLF2425M7L250P)
  3456
    Down East Microwave 3456-144
    California Microwave Amplifier
      8 Watts (Toshiba amp in the works for ~60 W)

## Slide 27: A Fresh Approach To A Multi-Band Microwave Station

## Slide 31: A Fresh Approach To A Multi-Band Microwave Station
Old Station
  903 MHz
    17.9 dBd Antenna Gain
    0.35 dB Feedline Loss
    3,982 Watts ERP
    1.05 dB System NF
  1296 MHz
    18.9 dBd Antenna Gain
    0.41 dB Feedline Loss
    2,472 Watts ERP
    0.71 dB System NF
  2304 MHz
    21.3 dBd Antenna Gain
    0.58 dB Feedline Loss
    4,721 Watts ERP
    1.58 dB System NF
  3456 MHz
    23.1 dBd Antenna Gain
    0.74 dB Feedline Loss
    1,722 Watts ERP
    1.74 dB System NF
New Station
  903 MHz
    13 dBd Antenna Gain
    2.2 dB Feedline Loss
    3,606 Watts ERP ( - 0.43 dB )
    0.5 dB System NF
  1296 MHz
    14.2 dBd Antenna Gain
    2.7 dB Feedline Loss
    2,119 Watts ERP ( - 0.67 dB @ 150W )
    3,531 Watts ERP ( + 1.55 dB @ 250W )
    0.5 dB System NF
  2304 MHz
    17.5 dBd Antenna Gain
    3.8 dB Feedline Loss
    188 Watts ERP ( - 14 dB @ 8W )
    5,861 Watts ERP ( + 0.94dB @ 250W )
    0.75 dB System NF
  3456 MHz
    17.5 dBd Antenna Gain
    4.6 dB Feedline Loss
    156 Watts ERP ( - 10.4 dB @ 8W )
    1,170 Watts ERP ( - 1.68 dB @ 60W )
    0.9 dB System NF

## Slide 32: A Fresh Approach To A Multi-Band Microwave Station
2014 January VHF SS (dead band January conditions)
  903 - 18 QSO’s x 11 Grid Squares (FN’s 20,30,31,32,34,41,42,43,44, FM’s 19,29)
    Best DX K1RZ FM19jh @ 306 Miles
    2nd Best DX N3NGE FN20bd @ 215 Miles
  1296 - 20 QSO’s x 10 Grid Squares (FN’s 20,30,31,32,41,42,43,44, FM’s 19,29)
    Best DX K1RZ FM19jh @ 306 Miles
    2nd Best DX N3NGE FN20bd @ 215 Miles
  2304 - 7 QSO’s x 3 Grid Squares (FN’s 31,32, 43)
    Best DX AF1T FN43cd @ 86 Miles
    Best DX Heard N3NGE FN20bd @ 215 Miles 539 didn’t hear me
  3456 - 1 QSO’s x 1 Grid Square (FN31)
    Best DX K1TEO FN31jh @ 60 Miles
  Most importantly I worked AA1I/R!!
    4 grids on 903 (FN31,32, 41,42)
    4 grids on 1296 (FN31,32, 41,42)
    2 Grids on 2304 (FN31,32)(he had a problem on 2304)
    0 Grids on 3456 (he had a problem on 3456)

## Slide 33: A Fresh Approach To A Multi-Band Microwave Station
Conclusions…
  Simple system
    One Feedline
    Small Antennas (really small)
    Wideband LNA is the only “electronics” on the tower
      Not available in past years…needed separate LNA’s
      Can be bypassed if “something happens”
    Transverters and Power Amplifiers are all in the shack
      High Power SSPA’s
        Continue to be come more available and or affordable
    Performance is (or can / will be) equivalent to the old system
      Higher performance can always be realized with larger antennas