## Slide 1: Design of Optimized Cassegrain Antenna Systems & Feedhorns
Paul Wade, W1GHZ ©2023

## Slide 2: Cassegrain Antenna Parabolic Dish with Hyperbolic Subreflector

## Slide 3: Cassegrain Antenna System
Cassegrain Antenna geometry
System Design
Examples & results
Feedhorns

## Slide 4: Why Cassegrain Antenna?
Reduce Feedline Loss
  Especially at Microwave bands
  Alternative is equipment at Dish Focus
Move equipment behind dish
  Reduce feedline loss
  Less weight at focus = better balance
Lower noise = higher G/T
  EME or Radio Astronomy
Illuminate Deep Dishes (f/D < 0.3)

## Slide 5: Lower noise – Spillover sees cold sky
Higher G/T for EME

## Slide 6: Cassegrain Problems
Big dish to be effective – larger than ~50
Hyperbolic Subreflector difficult to make
  CNC machining
  3D printing
More complicated design

## Slide 7: Simple case – Flat Subreflector at least 1 dB worse (with good feedhorn)
Not Possible
with very deep dish

## Slide 8: Hyperbola – Conic Section (slice thru cone) Two curves, mirror image

## Slide 9: Hyperbola Geometry & Equation Two Foci Ray from one reflects as though it came from other focus

## Slide 10: Cassegrain Antenna Geometry ►Single Hyperbolic curve ► One focus at Feedhorn phase center ► Other focus at Parabolic dish focal point ►Frequency independent

## Slide 11: Cassegrain Antenna Geometry Single Hyperbolic curve Radiation from Feedhorn at one focus reflects from subreflector as though it comes from dish Prime focus

## Slide 12: Casssegrain Antenna Design
Feedhorn Location
Subreflector Size
Calculate unique hyperbolic curve to reflect feed radiation to fully illuminate dish
Hyperbola parameters a, b, c
Note: 2c = Distance between foci
} Tradeoff

## Slide 13: Feedhorn Location and radiation angle determine Subreflector size
Moving feedhorn
back requires larger subreflector

## Slide 14: Feedhorn Location and radiation angle determine Subreflector size
Narrower Feedhorn beamwidth requires smaller subreflector

## Slide 15: Cassegrain good for deep dishes (no good prime feedhorns available)
Narrower Feedhorn beamwidth moves feed back – less blockage

## Slide 16: Feedhorn can be behind dish

## Slide 17: Casssegrain Design Procedure
Dish f/D
Feedhorn location
Feedhorn radiation angle
  At 10 or12 dB feed taper
Calculate subreflector size
ITERATE
Calculate Hyperbola a, b, c
Generate hyperbolic curve using hyperbola equation

## Slide 18: Cassegrain Design Tools
MATLAB routines
  Design calculations – quick iteration
  Hyperbola parameters (a, b, c) and curve
  G-code for CNC lathe or 3D printer
Perl script for antenna sketches
  Visual confirmation
Spreadsheet (updated)

## Slide 19: Subreflector machined on CNC Lathe

## Slide 20: Spreadsheet update - 2022
EME 2004 spreadsheet designed for equal diffraction and blockage loss
  Fine for large dishes
For amateur size dishes, subreflector > 10 preferred
Also tried to compensate for Space Attenuation
  Not needed with good feed simulation

## Slide 21: Examples
Working examples
  High microwave frequencies
  Scale-model performance
Performance test
  Measure peak signal on (long) antenna range
  Move subreflector out of beam
  Measure signal difference with feedhorn only
  Feedhorn gain is known or calculated

## Slide 22: Example 1 122 GHz Project by VK3CV 123 Diameter, 15.5 Subreflector, f/D = 0.25

## Slide 23: Feedhorn Large W2IMU Dual-mode horn High performance Easy to build

## Slide 24: 305 mm dish from Edmund Optics W2IMU Large Dual-Mode Feed 1.9 diameter by W1FKF

## Slide 25: 305mm dish with 3D printed removable Subreflector assembly Measurement: by VE2UG

## Slide 26: Example 2 – W1GHZ 48 Diameter, 12 Subreflector, f/D = 0.6 47 GHz

## Slide 27: DB6NT 47 GHz Transverter Separate horns for TX and RX (Skobolev 5.6) best DX 114 km

## Slide 28: 47 GHz Skobolev horn 5.6 dia ~23 dBi BW ~12º

## Slide 29: How about a waveguide switch Waveguide Spaghetti by VE3FN

## Slide 30: Machined Waveguide Switch Mates with DB6NT 47 GHz Transverter

## Slide 31: 47GHz zero Feedline loss SHF Micro 305mm dish Subreflector swings down Feedhorn ~23 dBi Dish adds 18 to19 dB ~ 50% efficiency

## Slide 32: Example 3 – W1GHZ 42 Diameter, 7 Subreflector, f/D = 0.375 10 GHz EME

## Slide 33: Example 4 96 Diameter, 20 Subreflector, f/D = 0.25 47 GHz Feedhorn ~14 dBi Dish adds 31.9 dB ~ 46% efficiency by VE2UG

## Slide 34: VE2UG 47 GHz Edmund dish

## Slide 35: Example 4 – VE2UG 47GHz
609mm dish (24 inches)
  Largest from Edmund Optic
W2IMU Large Dual-Mode Feed
  1.78 diameter
100mm Subreflector (15.7 )
PLAN: Compare Subreflectors
  machined metal
  3D printed

## Slide 36: Example 5 – DK7LJ 3 meter Diameter, f/D = 0.29 Large W2IMU feedhorn DL0SHF at 24 or 47 GHz

## Slide 37: Example 5 – DK7LJ 3 meter Diameter, f/D = 0.29 Skobolev feed (Ex 2) DL0SHF at 47 GHz

## Slide 38: Cassegrain Summary
Cassegrain Antenna performance demonstrated
Advantages for Large Dishes
Advantages for Deep Dishes
Reduce feedline loss at microwaves
Amateur fabrication possible
Design Procedure and Tools

## Slide 39: Feedhorns for Cassegrain Antennas
High Efficiency
Narrow Beamwidth => High Gain
Equal Phase Centers
Choices:
  W2IMU Dual-Mode
  Skobolev Optimum Dual-Mode
  Pickett-Potter

## Slide 40: W2IMU Dual-Mode Feedhorn
Simple Design
Range of sizes
1.31 Diameter – Original
1.22 to 1.95 Diameter
48º to 32º half-angle Beamwidth
Easy to machine for >47 GHz
30º Flare Angle if Length Adjusted

## Slide 41: Machine with 60º Center Drill for 30º Flare Angle

## Slide 42
Large W2IMU Dual-mode Feed Dimensions |  |  |  |  |  |  |  | 
 | with 30 degree flare angle |  |  |  |  |  |  | 
 |  |  |  | W1GHZ | Jan-23 |  |  | 
 | Input Waveguide diameter 0.7 to 0.8l |  |  |  |  |  |  | 
Frequency | Flare | Tool | Horn diameter |  | Horn Length |  | Gain | BW -10
 | degrees |  | inches | l | inches | l | dB | degrees
10.368 | 30 |  | 2.00 | 1.78 | 4.215 | 3.7 | 13.9 | 35
24.192 | 30 | #9 | 0.875 | 1.79 | 1.806 | 3.7 | 13.9 | 35
47.088 | 30 | #5 | 0.4375 | 1.74 | 0.928 | 3.7 | 13.9 | 35
76 | 30 | #3 | 0.250 |  | 0.439 |  | 13.9 | 39
78 | 30 | #3 | 0.250 | 1.65 | 0.439 | 2.9 | 13.1 | 39
122 | 30 | #2 | 0.1875 | 1.94 | 0.415 | 4.3 | 14.6 | 32
122 | 30 | 4mm | 0.157 | 1.63 | 0.281 | 2.9 | 13.1 | 39
241 | 30 | 2mm | 0.079 | 1.66 | 0.142 | 2.9 | 13.1 | 39
HDL_ANT | 25 |  |  | 1.78 |  | 3.5 |  | 
small IMU | 30 |  |  | 1.31 |  | 1.37 | 11.6 | 47

## Slide 43: 47 GHz, 1.74 Diameter

## Slide 44: Summary
Cassegrain Antenna performance demonstrated
Design Software available
Subreflector fabrication by CNC or 3D printing
Large W2IMU Dual-Mode Feedhorn easy to make
Works with inexpensive parabolic dishes
Some 122 GHz Feedhorns and Subreflectors available

## Slide 45
w1ghz.org