## Slide 1: JEY Labs
b
Doug Millar
K6JEY
Notes: Changes. More meters with BT
* HP improving the program with free Pathwave
* Prices going up*
*Keysight has redone the 34401 instruction and program to make it easier to use with a USB connection.
*Fluke still out of competition

## Slide 2: Data Logging With Modern Multimeters for Microwavers

## Slide 3: For Comparison
Fluke 8060A
1981 vintage
Does dB
relative to 600Ω
No data logging

## Slide 4: Rustrack Data Logging
This was easier than
Industrial units.
Most were digital
Versions of this with
Poor interfaces.

## Slide 5: Modern DMM’s
A lot is changing and will change.
  External data logging programs via
    USB, LAN, Bluetooth and Wi-Fi.
  Better displays
    TFT with excellent contrast
    Colors
    Much more information
  Firmware updates
  DBm measurements referenced to Z

## Slide 6: EME Measurement Examples
Use the Sun for antenna beam width measurements
Sun to cold sky or ground noise
Power measurement from the DC jacks/ recorder output on a power meter. (eg HP436, HP400EL)
Frequency drift over time on your radio.
Measurements can be in dBm or dBV at a fixed resistance and to a reference level.
  Auto scaled
  Saved
  Annotated
  Printed
  Use LAN /Wi-Fi or BT 5.3 for long distances from meter

## Slide 7: Focus of the Talk
7 Different meters
  Siglent SDM3045x 4 ½ digit (60K counts)
  Agilent 34410A 6 ½ digit
  Uni-T UT181A handheld 4 ½ digit. (60K counts)
  Uni-T UT 61E+ handheld 4 ½ digit (22K counts)
  Uni-T UT60BT Handheld (9.9k counts)
  AN9002 Handheld (6K counts)
  MEET Pencil DMM

## Slide 8: Siglent SDM3045,55,65
Very similar to an Agilent 34461A ($1,300+)
  Does data logging and trend analysis live. 1Gb of memory and thumb drive.
  Does dBm at Z or dBV
  Simple Recalibration
  1GB of memory +USB
  4 ½ digit $250
  5 ½ digit $350
  6 ½ digit $600

## Slide 9: Trend Display Data Logging

## Slide 10: Siglent dBm

## Slide 11: Siglent DMM Explorer Program

## Slide 12: DMM Explorer Trend Data Via USB

## Slide 13: Local Graph

## Slide 14: Agilent 34410A
Updated and improved
  34401a
Internal data logging
program via LAN.
Internal averaging
External BenchVue DMM prog via USB or LAN. Has excellent graphing. Use Connection Wizard program
dBV or dBm ref. to Z. is easy. Get free basic version.
About $450

## Slide 15: Keysight BenchVue
First rate program
Averaging gives you one more digit (34461a)
Get Pathwave as a free download.
Regular BenchVue is $65/yr.
LAN and USB connections are easy
LAN can conflict with Wi-Fi.

## Slide 16: Pathwave DMM Free version

## Slide 17: BenchVue DMM Paid App and 34410A

## Slide 18: HP34410a Remote Mode
Run LAN/USB cable to computer in BenchVue DMM app. (Use Connection Expert.)
LAN to portable Wi-Fi router should also work
Great for working on antennas and monitoring the radio.

## Slide 19: Agilent 34401a Notes
34401a
  Uses a Null Modem-DB9 connection.
  Startech.com FTDI to null modem DB9 adapter cable should work. $45
  Keysight serial cable instructions-
Keysight Serial cable Instructions
  Meter will measure dBm.
  Excellent meter but 1993 vintage

## Slide 20: UNI-T 181A
Hand held
Bigger than average.
Excellent sharp display
Extensive data recording
Accurate and very fast
External USB/Bluetooth
Firmware upgradable
Recording and graphing
are internal and External.
  About $280

## Slide 21: Relative dBm at Z and Record
DBM referenced to Z

## Slide 22: Save and Trend Views

## Slide 23: UT181A
Data Logging
Use either
Internal data display or
External program via USB
Or via Bluetooth to Android
Easy set up! Live graphing.
Record data then get graph.
Use up and down to scale graph.
dBV or dBm
20,000 data point memory.

## Slide 24: Software for UT181A
Auto ranges and records live
Close or open windows here

## Slide 25
UT181 dBm Measurement Chart

## Slide 26: UNI-T Program Notes
Chart can be full screened. Auto scaled.
Window sections can be opened or closed.
The Bluetooth programs are excellent.

## Slide 27: Bluetooth Adapter
Works well with
UNI-T and Android
or Apple
Data program
BT 4.0
Adapter $30

## Slide 28: UT 181A via Android
Recording live
in dBm
Try- the meter
at the radio
and
The Android
at the antenna
Data saved on
Phone and DMM
You don’t have
To be at the
Meter to read it!!

## Slide 29: UNI-T 61E+
UNI-T 61E+ $85
  Very accurate excellent Meter.
  Has Relative measurement
    Relative AC V measurement
    No dBm measurement
    No internal data logging
  Has same Bluetooth adapter
  and excellent program.
  22,000 counts
  $250 cheaper than UT 181

## Slide 30: Android display Via Bluetooth
For dBV readings
1.Zero with relative button
in AC volts position.
2.Observe peak hold on chart.
3.Calculate dBm from AC
voltage difference.
Comes with calibration cert.
4. Order one that comes with a
case.

## Slide 31: Uni-t UT60BT
Very cheap at $40
Internal Bluetooth
More limited
Same program
9.9k counts

## Slide 32: AN9002
Cheap at $28
Excellent ext. Program
Internal Bluetooth
Slippery case.
Cheap leads
Display Lens not protected.
Good display, though.
6k counts

## Slide 33: MEET- Pencil DMM
  Relative and hold
  Bluetooth for external
  analog type meter.
  “ DMM
  without test leads”
  Data logging,
  and graphing
  Takes pictures of the
  setup.
  $35 Amazon
“MSBDTP1A”

## Slide 34: Meter and Phone
Turn the phone
clockwise for this display
Turn it anticlockwise
and get the graphing
display.
You can take pictures of
the measurements.
No test lead wires!
Did I say $35 from
Amazon?

## Slide 35: Extra ANENG 681
Color model available
Form factor of phone
USB charging
Excellent display
Auto function
Well built and sturdy
$26 Best Bang/$

## Slide 36: EME Measurement Examples
Use the Sun for antenna beam width measurements
Sun to cold sky or ground noise
Power measurement from the DC jacks/ recorder output on a power meter.
Frequency drift over time on your radio.
Measurements can be in dBm or dBV at a fixed resistance and to a reference level.
  Auto scaled
  Saved
  Annotated
  Printed
  Use LAN /Wi-Fi or BT 5.3 for long distances from meter

## Slide 37: Meter Comparison- Expensive
Siglent 3045x- $250
  Best display and easiest to use, thumb drive storage
  Uses USB for remote program that works easily
Agilent 34410A- $450
  Best accuracy, internal program hard to use. Outstanding ext. program BenchVue Basic (live graphing) LAN or Wi-Fi- USB
UT181A $290
  Hand held, versatile, great display, accurate, many measurements and very fast. Unique bar graph.
  Internal graph, easy and excellent interface and program
  Graph after data on meter, but same time in ext. program
  Bluetooth app works perfectly for Android and Apple.
UT61E+ $85
  Like the 181- but no internal data logging or dBm.
  Use Bluetooth and ext. program and ACV for logging.

## Slide 38: Meter comparison- Cheap
Uni-t UT61BT- $37
  Well built , good range, internal BT Good prog.
AN9002- $28
  Cheaply made, Great Prog. internal BT
Pencil DMM- $35
  A no brainer. No test lead DMM. Buy it.

## Slide 39: Conclusions
The Siglent 3045x is an excellent lab meter with an easy to use USB program. Thumb drive storage.
A good combination for bench and portable are the Siglent 3045x and UT61E+
If you bought just one meter, the Uni-T 181A would be a good choice.
Buy the Pencil DMM for $35. No brainer.

## Slide 40: Results
Worthwhile changes-
  The addition of data logging and graphing programs.
  USB and LAN connections that are easy to use.
  Remote program via Bluetooth to phone.
Next Steps?
  More phone based apps via Bluetooth 5.3
  Wi-Fi to router to a laptop’s Wi-Fi input to run
    Programs via Wi-Fi.

## Slide 41: Time for Questions
Doug Millar K6JEY
drzarkof56@yahoo.com