## Slide 1: 5 bands in 2U
Or maybe 8 bands in 3U
Or 10 in 4U
(if you don’t count HF)
(Or amplifiers)

## Slide 2: In The Beginning
There were W1GHZ Cheap and Simple Transverters
  FT-817
  2 GHz & 3 GHz
+
+
+

## Slide 3: In The Beginning
There were W1GHZ Cheap and Simple Transverters
  2 GHz & 3 GHz
=
+

## Slide 4: In The Beginning
There were W1GHZ Cheap and Simple Transverters
  5 GHz
  And a 10 GHz (DEMI)

## Slide 5: And a Whole Bunch of Carrying Cases

## Slide 6: Time to Consolidate!
Keep the 817 and W1GHZ transverter modules
  W1GHZ - 900, 1296, 2 GHz, 3 GHz, 5 GHz
  DEMI – 10 GHz
Add in
  GPSDO
  Frequency flexible PLL
  Waterfall / FT8 / Digital subsystem

## Slide 7: System Design
900 MHz
Transverter
1296 MHz
Transverter
2.3 GHz
Transverter
3.4 GHz
Transverter
5.7 GHz
Transverter
Band Switch
1:6 SMA Relay
1:6 SMA Relay
Raspberry Pi
SPI
LCD w touchscreen
USB/TTL
Cat
IF
GPSDO / PLL
GPS Antenna
RF In/Out
Kbd
USB SignaLink
USB
PTT
Sequencer
FT-817

## Slide 8: 5 Supplies, 3 voltages per transverter, 5 transverters, Tx or Rx mode
Select
Always On
On for RX
On for
TX

## Slide 9: Plus a whole bunch of FET switches with selection logic
TX/RX
Select 0 to N
…

## Slide 10: Is one metric &^$%# ton of jumpers

## Slide 11: As soon as it was done….
Murphy arrived!
  Adding another transverter
  Need another voltage
  Sequencer complexities
    Preamp considerations
    Amplifier considerations

## Slide 12: Has To Be an Easier WayTM !
Simple FET Switch board
TR/RX1
Select1
FET Sw
Out1
Vin1
FET Sw
Out3
Vin3
FET Sw
Out2
Vin2

## Slide 13: Somewhat simpler
Transverter
FET Switch
IF
TX Out
RX In
Tx/Rx (PTT)
Select
TxV
RxV
AoV

## Slide 14: Familiar FET Power Switch
Using a slightly different transistor
F9Z24NS
SMD mount, -55V-2300V
15V VGS
Got a tube of parts @ MUD Banquet!

## Slide 15: System Design V2
900 MHz
Transverter
1296 MHz
Transverter
2.3 GHz
Transverter
3.4 GHz
Transverter
5.7 GHz
Transverter
Band Switch
1:6 SMA
Raspberry Pi
SPI
LCD w touchscreen
USB/TTL
Cat
IF
GPSDO / PLL
GPS Antenna
RF In/Out
Kbd
USB SignaLink
USB
PTT
Sequencer
FT-817
1:6 SMA
Select 1-5
Tx/RX
T/R
T/R
T/R
T/R
T/R

## Slide 16: GPSDO + PLL + RasPI
LARS GPSDO 10MHz reference
  Arduino
  Common off the shelf GPS module – RS232 interface
ADF4351 PLL Synthesizer - 35MHz to 4.4 GHz
  Arduino reference designs available
  RasPI reference design available
    https://github.com/davecrump/RPiADF4351

## Slide 17: GPSDO + PLL
LARS GPSDO 10MHz reference
  Arduino
  Common off the shelf GPS module – RS232 interface
ADF4351 PLL Synthesizer - 35MHz to 4.4 GHz
  V1.0 Arduino based
  V2.0 RasPI
    ADF4351 reference design available
    https://github.com/davecrump/RPiADF4351

## Slide 18: GPSDO + PLL
Lars GPSDO
  Arduino + GPS module + cheap 10 MHz OXCO
  Code and schematics
    https://www.eevblog.com/forum/projects/lars-diy-gpsdo-with-arduino-and-1ns-resolution-tic/
  Built as stand-alone without display. Modified code to pass status to 2nd Arduino

## Slide 19: GPSDO
Arduino
COTS GPS Module
FTDI
USB/
RS232
1pps
10MHz OXCO
DAC1 out
10 MHz
Counter
PLL
/10 – 1MHz
/2 – 5MHz
USB
(optional)
Lock

## Slide 20: GPSDO

## Slide 21: PLL V1.0
Arduino
COTS ADF4351 Module
FTDI
USB/
RS232
I2C
10MHz OXCO
10 MHz
35MHz – 4.4 GHz Out
USB
(optional)
Frequency
Select
2 line x 16 char
LCD Display
I2C
Interface
Lock

## Slide 22: PLL V1.0
I2C LCD Display interface
eBay - $1
FT232RL FTDI Serial Adapter Module
eBay - $1.25
Arduino Mini Pro
eBay - $3.13
GPS Module
eBay - $2.79
10MHz VCOCXO Module
eBay - $12
Raspberry Pi Zero 2 W
eBay - $22

## Slide 23: PLL V2.0
COTS ADF4351 Module
I2C
10MHz OXCO
10 MHz
35MHz – 4.4 GHz Out
USB
Band
Select
Lock
Keyboard
Touchscreen
HDMI
Pi 3 or 2W

## Slide 24: Future work
Tidy up before June & train user
Post June 2024
  Dish/Feed switch to demultiplex the feed line
  Preamplifier Deck – Need to put in drop/insert ports
  Amplifier Enclosure – Won’t fit in road case and be portable
  220 MHz transverter
  24 GHz narrow band?