## Slide 1: Synthesizers for Amateur Radio NEWS Conference 2025 - WA1MBA
RECENT EXPERIENCE WITH SYNTHESIZERS

## Slide 2: Talk Outline
Which Synthesizers ?
Synthesizer Innards
Tests performed
Results
Summary

## Slide 3: Four Synthesizer Groups
Source
Specs
Cost pre Tariff
HP
Used
8341B
10 M to
20 G
$20K New
$2+K Used
Valon
Tech
5019
10 M to
20 G
$2.5K
New
Kuhne
MKU
8-13
AD5355
54 M
To 13+G
€490
New
China
Ebay
AD5355
54 M
To 13+G
$ 120
To $170
New
CH3
CH1
CH2

## Slide 4: There are others
AD 4351 and 5355 “Eval Boards” with and without controllers, HMC833, TI, Linear etc.
Home Brew boards by Hams, with and without controllers (SV1AFN and others)
Other companies similar to Valon Tech
The big boys who rightfully get big bucks, state of the art, bullet proof, supported
  Keysight (Agilent, HP)
  Rhode & Shwarz
  Anritsu (Wiltron)
  Tektronix…

## Slide 5: The Chinese devices had no Instructions or Labels (Except One)
On the first Chinese unit, I measured what was coming out of the ports and figured out which was the fundamental (and could do division) and which was the multiplied (doubled) output
The other Chinese units had similar arrangements, so I quickly found those ports
10 MHz Reference input?
  One took the 10 MHz reference as-is
  One required removal of a solder bridge
  One required removal of a zero ohm resistor but still did not lock, even at the original 125 MHz

## Slide 6: Port and Frequency (CH1)
A
B
3.5 to 6.5 GHz
7 to 13 GHz

## Slide 7: Connections, Control (CH1) “ADF5355 V3 13.6 GHz RF Signal Generator Core Board Sweep Frequency +STM32 Board”
OUTPUT
PORT A
Fundamental
And Divided
OUTPUT
PORT A
Terminate
OUTPUT
PORT B
Doubled
USB C
REF A
10 MHz In
SEE MOD
Ref -
Leave Open
Move Cursor L R
Change Value
US $145 Ebay 4/2025
DC In
6 V

## Slide 8: Remove Solder Bump from jump to enable external Ref on this Board 10 MHz works great into “CLK-A”

## Slide 9: Another Ebay Chinese Model (CH2)

## Slide 10: Remove Internal 10MHz Osc and Wire to Internal Socket File hole above DC to let thin coax out to SMA for 10 MHz
REMOVE
ADD

## Slide 11: Talk Outline
Which Synthesizers ?
Synthesizer Innards
Tests performed
Results
Summary

## Slide 12: Architecture
All these synthesizers are meant to cover up to either 13.6 or 20 GHz
With one exception (the HP 8341B), they are based on modern PLL VCO IC’s
What is a PLL VCO Synthesizer IC?
What is important about them?
How are they controlled?

## Slide 13: PLL Synthesizer

## Slide 14: The AD 5355 PLL Synthesizer

## Slide 16: Talk Outline
Which Synthesizers ?
Synthesizer Innards
Tests performed
Results
Summary

## Slide 17: Tests to Understand these Synthesizers
Tried to lock them to 10 MHz
Looked at several frequencies
  Wide span
  Close span
  Very Close
  Can see total Phase & Amplitude noise)
Looked at some of the sub harmonics and harmonics
Did not perform Phase Noise Plots
  Only looked down -50 to -100dBc on Spectrum Analyzer
You may look up phase noise online if you want

## Slide 18: Did NOT Test for Phase Noise Find them on the web
W1GHZ, Dubus, Others

## Slide 19: Compared Across Synth’s for Each Test
 | HP 8431B | MKU 8-13 PLL LO | VALON 5019 | Ebay Small “ CH1” | Ebay Large “CH2”
12960 Wide and Close |  |  | * |  | 
8 GHz Wide and Close |  |  |  |  | 
1152 Wide and Close |  |  |  |  | 
Sub Harmonics |  |  |  |  | 
Harmonics |  |  |  |  | 

## Slide 20: Talk Outline
Which Synthesizers ?
Synthesizer Innards
Tests performed
Results
Summary

## Slide 21: 12,960 Wide
MKU
CH1

## Slide 22: 12,960 (and 19.4*) Closeup
MKU 12.9
CH1 12.9
Valon 19.4

## Slide 23: 12,960 Closeup
CH1

## Slide 24: 12,960 Closeup
MKU

## Slide 25: 19,440 Closeup
Valon 19.9

## Slide 26: 8 GHz Wide
HP
CH1
CH2

## Slide 27: 8 GHz Closeup
HP
CH1
CH2

## Slide 28: 1152 Wide
MKU
HP
CH1
CH2

## Slide 29: 1152 Close
MKU
HP
CH1
CH2

## Slide 30: 1152 Vey Close CH1

## Slide 31: 1152 Very Close MKU

## Slide 32: 1152 Very Close VALON

## Slide 33: Harmonics and Subharmonics
Except for the HP, all the IC synthesizers rely on a master (PLL) Fundamental Oscillator and
  multiplication for the highest frequency range
    e.g. 4 to 6.5 GHz VCO yields 8 to 13 GHz output
  no multiplication for the next lower portion
    e.g. 4 to 6.5 GHz (the fundamental VCO)
  division for the lowest ranges
    e.g. .054 to 4 GHz (dividing the fundamental)
Some Synthesizers have two ports, one for the top band, and another for the lower bands
There can be leakage of the wrong harmonics or subharmonics present

## Slide 34: Harmonics – Valon @ 1.152 to 10

## Slide 35: Harmonics – Valon @ 1.152 to 24
X1
X4
X2
X9
X10
X11
X12
X13
X17
X18
X21
8x = 9216 = Fund
Nothing
2X Fund = 1.4
Nothing

## Slide 36: Harmonics – CH2 1152 at 24192
24.192GHz
-104 dBc

## Slide 37: Harmonics – MKU @ 10 GHz Includes Harmonics of 5 GHz Subharmonic (fund)
10GHz
+15dBm
25GHz
-33dBm
20GHz
-2dBm
15GHz
-5dBm

## Slide 38: Subharmonic Leakage of MKU @ 10 GHz = <-60dBc
5GHz
Under noise

## Slide 39: Subharmonic Leakage MKU @12 GHz = -47dBc

## Slide 40: Explain Low Fundamental Leakage but Significant Harmonics of Fundamental
MKU has an excellent filter in place to remove subharmonics – which are really the fundamental of the VCO
However, it does generate harmonics of the VCO even though the user is asking for the second harmonic of the VCO in the 8-13 GHz (Primary output range)
Therefore, harmonics of the (fundamental) VCO appear in the nicely filtered output

## Slide 41: Explain Low Fundamental Leakage but Leakage of Harmonics of Divided Fundamental
Just an Educated Guess
  Division of Frequency is a naturally non-linear process
  Therefore, the divided frequency is rich in harmonics while the fundamental is not
  These divided fundamentals will cover a large frequency range and therefore cannot easily be filtered

## Slide 42: Harmonics & Subharmonics
Subharmonics suppression (F0 leakage)
  Valon -15 to -26dBc
  MKU -47 to below noise
  CH1 -2.6 to -19.5 dBc
  CH2 not measured
Harmonic Suppression of Divided F0
  Valon Almost no suppression
  MKU Almost no suppression
  CH1 No suppression
  CH2 not measured

## Slide 43: You might want to use a filter
Pipe Cap W1GHZ Pipe Cap Filters Revisited
Band Pass, 2 GHz through 10 GHz easy and well documented

## Slide 44: Minicircuits Filters (hundreds) Plenty of Highpass and Bandpass

## Slide 45: Filters, High Pass Good to 11 or 13 GHz $32

## Slide 46: Filters – High Pass Good to 20 GHz $210

## Slide 48: Talk Outline
Which Synthesizers ?
Synthesizer Innards
Tests performed
Results
Summary

## Slide 49: Summary
 | HP 8431B | VALON TECH 5019 | MKU 8-13 PLL LO | EBAY CHINESE 2 Unit Similar AD5355
Wide Spectrum Quality | Excellent Final Floor extremely low | Excellent Final floor Very low Up to 20 GHz | Excellent Final floor very low | Good to Fair Some -40dBc Spurs Worse at Fractional F0
Narrow Spectrum Quality | Excellent Close in | Excellent Close in -55dBc 1KHz -80dBc | Excellent Close in -45dBc 1KHz -80dBc | Quite Poor Most Freqs ~Spurs -30dBc ~1KHz Floor -45dBc
Sub-harmonic Leakage | None | -15dBc To -26dBc | -47dBc To under noise floor | -4dBc to -19.5dBc
Harmonic | Not Measured | Not Measured | 3F0 -20dBc 5F0 -48dBc | 0dBc

## Slide 50: Valon Programming
USB – Full Configuration Manager
  Runs on PC
  Set Frequency, Freq List, Sanning, Look at and modify Registers
Ethernet – Most of Configuration Manager
  Enter Frequency, Choose from List
  Web Based, can operate from phone!

## Slide 51: Programmer MKU Old School
$100 - BUT
Appears that
Newer Display
No longer
Compatible

## Slide 52: Programmer MKU New School
$400
The NEW
Kuhne Way

## Slide 53: Advice to Fix Chinese 5355

## Slide 56: SV1AFN.COM

## Slide 57: Summary cont.
OBJECTIVE CHARACTERISTICS | CHOICE & CONSIDERATIONS | COST
Cheap, 8-13.8 GHz, Low Power, Spurs below -30 dBc All Frequencies but with spurs | Chinese Ebay Prefer #2 for Performance Prefer #1 for Cost | $100 to $170 Pre-Tarriff Consider Filters Look at Improvements
Affordable High Quality LO Solid, Tough | Kuhne MKU 8-13 PLL LO | $450 + another $400 for Programming Maybe a $30 Filter
Bench Source Run from PC or Phone | Valon 5000 series, 5019 goes to 20 GHz Also 8 and 30 GHz | $2500 and might want a $400 Filter
Bench Source works with other HP Equip for Scalar Analysis | HP 3431B or similar Not Portable | Used in the $2K to $4K Range. 5x that calibrated w guaranty