## Slide 1: VHF SUPER CONFERENCE APR 26-28, 2019 WASHINGTON-DULLES By: Ben Lowe, K4QF/K4VOW
IMPEDANCE MATCHING 101

## Slide 2: WHY IMPEDANCE MATCH?
FOR TRANSMITTING - Impedances are necessarily matched to enable efficient power transfer from one device to another, such as an output amplifier to an antenna or a driver amplifier to an output amplifier.
FOR RECEIVING – A low noise preamplifier is designed to achieve its minimum noise figure for a particular source or driving impedance. The antenna must be matched to this impedance to achieve the minimum noise performance.

## Slide 3: THE CASE FOR 50 OHMS
A common impedance used for Amateur Radio applications is 50 ohms
The feedlines, i.e. the coax, are designed for 50 ohms, a common standard impedance.
The power amplifiers are designed to operate into a 50 ohm load, i.e. the antenna fed with 50 ohm coax.
The receiver preamps are designed to achieve minimum noise figure with a 50 ohm driving source; i.e. the antenna/feedline.

## Slide 4: THE THREE ELEMENTS OF IMPEDANCES
The resistor, R
The inductor, L
The capacitor, C

## Slide 5: THE BASICS, THE IMPEDANCE OF EACH COMPONENT
Z =R
Z = +jXL |Z| = |XL|
Z = -jXC |Z| = |XC|

## Slide 6: THE IMPEDANCE OF EACH COMPONENT
|XL| =,
where: frequency in Hz
inductance in henries
|XC| =
where: frequency in Hz
capacitance in farads
and

## Slide 7: THE COMPLEX IMPEDANCE
+jXL
Z = R + jX
R
Z = R - jX
- jXC
θ

## Slide 8: EXPRESS , , AND USING SCIENTIFIC NOTATION
SHORT CUTS
x 1000 = x 103
1/1000 = x 10-3
= 6.28
= 0.159 = 159 x 10-3
x 106
144 x 106 Hz)
10-9 henries = nanohenries, nH
10-12 farads = picofarads, pf

## Slide 9: MORE BASICS
The loaded Q = Xs/Rs = Rp/Xp
A series R & X circuit has an equivalent
parallel R & X circuit.
Xs is the series reactance,
Rs is the series resistance,
Rp is the parallel resistance,
Xp is the parallel reactance.

## Slide 10: HELPFUL HINTS
Do not try to match more that a 4:1 impedance transformation. If you have to match over a larger impedance ratio, use two or more matching sections.
Before using a series L or series C, look at your design. If you need a d.c. blocking capacitor, use your matching C for this d.c. block. If you need to feed d.c. to a circuit component, use an L for this as part of the matching circuit.

## Slide 11: HELPFUL HINTS (con’t)
Use complimentary L sections for broader bandwidth and higher impedance transformations; i.e. a two stage match.
Always match low to high impedances to simplify calculations. If you need to match a high impedance to a low impedance, do the calculations for low to high. Then remove the low impedance and connect the high impedance. The matching circuit is reciprocal and works both ways.

## Slide 12: COMPONENT CALCULATIONS
=
A series impedance has an equivalent parallel impedance. Both the series and parallel circuits have the same Q, and:
Rp = Rs (Q2 + 1) (Remember this!!!)

## Slide 13: EXAMPLE 1 – COMBINING FOUR ANTENNAS
Match 50 ohms, such as an antenna, to 200 ohms. Rs = 50 ohms, Rp = 200 ohms.
Calculate Q from Rp = Rs (Q2 + 1).
Q2 + 1 = (200/50) = 4,
Q2 = 3, Q = 1.732
Since Q = Xs/Rs,
Xs = Q * Rs = (1.732 * 50) = |86.6| ohms.
For a series inductor, the circuit is 50 + j86.6 ohms.
Q also = Rp/Xp, and Rp = 200 ohms.
Therefore, Xp = Rp/Q = 200/1.732 = +j115.5 ohms.

## Slide 14: COMBINING FOUR ANTENNAS (con’t)
+j 86.6 ohms
50 ohms = +j115.5 ohms 200 ohms.
Now place – j115.5 ohms in parallel with +j115.5 ohms leaving only the 200 ohm real impedance.

## Slide 15: COMBINING FOUR ANTENNAS (con’t)
200 ohms +j115.5 ohms -j115.5 ohms
Since +j115.5 ohms in parallel with –j115.5 ohms = ∞,
resulting in:
200 ohms

## Slide 16: COMBINING FOUR ANTENNAS (con’t)
Final matching circuit
+j86.6
50 -j115.5 = 200 Ω
Component calculation for +j86.6 at 144 MHz:
|86.6| = = 6.28 * (144 * 106) *
= 95.8 nH
Component calculation for –j115.5 at 144 MHz:
|115.5| = = (159 * 10-3)/ (144 * 106) * C, so:
C = 9.6 * 10-12 = 9.6 pf.

## Slide 17: COMBINING FOUR ANTENNAS (con’t)
50 Ω
95.8 nH 95.8 nH
50 Ω 50 Ω
9.6 pf 9.6 pf
95.8 nH 95.8 nH
50 Ω 50 Ω
9.6 pf 9.6 pf
or
95.8 nH 50 Ω 95.8 nH
50 Ω 50 Ω
95.8 nH 38.4 pf 95.8 nH
50 Ω 50 Ω

## Slide 18: COMBINING FOUR ANTENNAS SIMPLIFIED
12.5 Ω
Make all feedline the exact same length. Now match 12.5 Ω to 50 ohms using a series inductor and parallel capacitor.
Rp = Rs (Q2 + 1), Q = 1.732, Xs = 23.9 nH, C = 38.2 pf.
12.5 Ω 23.9 nH 38.2 pf. = 50 Ω

## Slide 19: COMBINING FOUR ANTENNAS SIMPLEFIED
23.9 nH
50 Ω
38.2 pf

## Slide 20: WHEN IS YOUR INDUCTOR 23.9 nH?
23.9 nH 36 pf
50 Ω
= )
To account for 9 nH of internal lead inductance for the 36 pf capacitor:
L = 29.4 nH + 9 nH = 38.4 nH, and
ANTENNA ANALYZER

## Slide 21: WHEN IS YOUR INDUCTOR 23.9 nH, con’t?
29.4 nH 9 nH 36 pf
50 Ω
= ) +j32.6 -j32.6
|XL| =
|XL| = +j 32.6
|XC| = )
|XC| = -j 32.6
@ 135.2 MHz: +j32.6 –j32.6 + 50 = 50 Ω
ANTENNA ANALYZER

## Slide 22: USE COMPLEMENTARY L MATCHING FOR HIGHER IMPEDANCE TRANSFORMATIONS
EXAMPLE 2 – Multi step impedance transformation
Solid state PA device typically is ~ 4 Ω. Since this is > 4:1 (50/4 = 12.5), use two impedance transformations and use complementary L sections: i.e. if first transformation is series L and parallel C, the second transformation should be series C and parallel L.
Also, the interstage impedance should be the “geometric mean” impedance for the same percentage step to the beginning and ending impedance values.

## Slide 23: DETERMINE THE “GEOMETRIC MEAN” IMPEDANCE
The geometric mean impedance = = 14.14 Ω. The 1st stage impedance ratio is 14.14/4 = 3.535, and the 2nd stage impedance ratio is also 50/14.14 = 3.535; both less than 4:1!
1st stage transforms 4 Ω to 14.14 Ω with an inductor.
Rp = Rs (Q2 + 1), 14.14 = 4(Q2 + 1), Q = 1.59.
Q = Xs/Rs, Xs = Q*Rs = (1.59*4) = +j6.36
Xp = Rp/Q = 14.14/1.59 = +j8.9 Ω
Therefore, use –j8.9 Ω to resonate +j8.9 Ω.
4 Ω +j6.36 Ω -j8.9 Ω = 14.14 Ω

## Slide 24: 2nd STAGE TRANSFORMATION TO 50 OHMS
2nd step transforms 14.14 Ω to 50 Ω with a capacitor.
Rp = Rs (Q2 + 1), 50 = 14.14(Q2 + 1), Q = 1.59.
Q = Xs/Rs, Xs = Q*Rs = (1.59*14.14) = -j22.5
Xp = Rp/Q = 50/1.59 = -j31.44 Ω
Therefore, use +j31.44 Ω to resonate -j31.44 Ω.
4 Ω +j6.36 Ω -j8.9 Ω -j22.5Ω +j31.44 = 50 Ω

## Slide 25: DETERMINE COMPONENT VALUES FOR 144 MHZ
+j6.36 Ω = 7 nH
-j8.9 Ω = 123.4 pf
-j22.5 Ω = 49 pf
+j31.4 Ω = 34.7 nH
4 Ω 7 nH 123.4 pf 49 pf 34.7 nH 50 Ω

## Slide 26: UNBALANCED POWER DIVIDER
EXAMPLE 3: USED TO DIVIDE POWER FOR UNEQUAL LEVELS AND MAINTAIN 50 OHMS FOR EXCITER.
50 Ω, 100 watts 50 Ω, 40 watts
50 Ω, 60 watts
Exciter has 100 watts output. PA requires 40 watts. Need to dissipate 60 watts into 50 Ω termination and still present 50 ohm load to the exciter.
50 MHz Exciter
UNBALANCE
DIVIDER
POWER AMPLIFIER

## Slide 27: UNBALANCED POWER DIVIDER, con’t
Determine impedances for desired power split.
50 Ω, 100 watts V R1 40 watts R2 60 watts
, ,

## Slide 28: UNBALANCED POWER DIVIDER, con’t
Substituting 1.5 R2 for R1
,
= 1.5 2
= 125
= 83.3 Ω
= 125 Ω
The 50 Ω input to the PA should be matched to 125 Ω, and the 50 Ω input to the termination should be matched to 83.3 Ω.

## Slide 29: UNBALANCED POWER DIVIDER, con’t
For the PA side to match 50 Ω to 125 Ω :
Rp = Rs (Q2 + 1), 125 = 50(Q2 + 1), Q = 1.22.
For a series capacitor, Xs = Q*Rs = (1.22*50) = -j 61, and Xp = Rp/Q = 125/1.22 = -j102.5 Ω.
For the 50 Ω termination side to match 50 Ω to 83.3 Ω:
Rp = Rs (Q2 + 1), 83.3 = 50(Q2 + 1), Q = 0.82.
For a series inductor, Xs = Q*Rs = (0.82*50) = +j41, and Xp = Rp/Q = 83.3/0.82 = +j101.6 Ω.
Since the parallel reactance toward the PA is –j 102.5 and the parallel reactance toward the termination is +j101.6, i.e. approximately the same, these can be used to compensate for each other with the parallel combination!

## Slide 30: UNBALANCED POWER DIVIDER, con’t
50Ω -j61 = 125 -j102.5 +j101.6 83.3 = +j41
PA in 50 Ω
load
125 83.3 +j11,571 = 50 Ω
36.9 μH

## Slide 31: FINAL UNBALANCED POWER DIVIDER CKT.
@ 50 MHz:
-j61 Ω +j41 Ω
40 watts 60 watts
to PA to 50 Ω
52 pf 130 nH load
100 watts from
transceiver

## Slide 32: I AND Q GENERATION FOR SDR OR SSB
EXAMPLE 4: GENERATION OF I AND Q SIGNALS
@ 144 MHz:
50 Ω VO∠+45, I (0°)
+j50 in
50 Ω VO∠-45, Q (90°)
-j50 in
144 MHz Oscillator
Mini-Ckts
GALI-55+
Mini-Ckts
GALI-55+

## Slide 33: I AND Q GENERATION, con’t
50Ω -j50 = 100 -j100 +j100 100 = +j50 50 Ω
100 100 = 50 Ω

## Slide 34: I AND Q GENERATION, con’t
@ 144 MHz:
50 Ω VO∠+45, I (0°)
+j50 in
55 nH
50 Ω VO∠-45, Q (90°)
-j50 in
22 pf.
144 MHz Oscillator
Mini-Ckts
GALI-55+
Mini-Ckts
GALI-55+

## Slide 35: SM6PGP/SM6FHZ CIRCULAR POLARIZATION

## Slide 36: 1296 MHz QUADRATURE COUPLER
@ 1296 MHz: -j25 Ω 25 Ω
50 Ω PO∠ 0°
4.9pf 50 Ω
+j50 Ω
6.1 nH
50 = 25(Q2 + 1)
Q = 1 = Xs/Rs = Rp/Xp PO∠ -90°
Xs = -j25 Ω 50 Ω
Xp = +j50 Ω
λ/4 50 OHMLINE

## Slide 37: 1296 MHz QUADRATURE COUPLER

## Slide 38: LNA OPTIMUM SOURCE IMPEDANCE
EXAMPLE 5: DESIGN INPUT MATCH FOR MINIMUM NF
Typical source impedance from min. NF contour on Smith Chart:
Min. NF source
Impedance =
0.82 +j 0.18 (normalized)
= 41 + j9
∴ load impedance =
41 - j9, complex conjugate
Q = 0.22, Q2+1 = 1.048
Rp = Rs(Q2+1)
= 41*1.0484) = 43
Xp = Rp/Q = 43/0.22
= -j186

## Slide 39: LNA OPTIMUM SOURCE IMPEDANCE, con’t
Use +j186 to resonate –j186. At 1296 MHz, +j186 =
0.023 μH or 23 nH, yielding:
- +j9 = 43 -j186 43 -j186 +j186
Leaving 43 Ω
This is sufficiently close to 50 Ω, or a λ/4 line ( can be added between the 43 Ω and 50 Ω input to achieve the 50 Ω match. (This would be academic.)

## Slide 40
SUMMARY
EXAMPLE 1: Combining 4 antennas
EXAMPLE 2: Two step impedance transformation for
greater impedance ratios
EXAMPLE 3: Unbalance power divider
EXAMPLE 4: Generation of I and Q signals
EXAMPLE 5: LNA input circuit for minimum noise figure

## Slide 41
QUESTIONS?