## Slide 1: The Quagi Revisited

## Slide 2
The Quagi was originally designed on the K6YNB/N6NB-Wayne Overbeck backyard antenna range in 1972, with the assistance of Will Anderson, WB6RIV/AA6DD (check out the 1972 photo of Will at the end of this article). Later work on the larger Quagi designs was done in a city park and on a beach in an attempt to get away from reflections and obstructions that made the task of optimizing the antenna design in a small backyard more difficult. What originally inspired the development of the Quagi antenna was the need for a low-cost, high-gain antenna for moon-bounce communications.
http://n6nb.com/quagi.htm

## Slide 3
Some Quagi history
The Quagi was originally designed on the K6YNB/N6NB backyard antenna range in 1972, with the assistance of Will Anderson, WB6RIV/AA6DD (check out the 1972 photo of Will at the end of this article). Later work on the larger Quagi designs was done in a city park and on a beach in an attempt to get away from reflections and obstructions that made the task of optimizing the antenna design in a small backyard more difficult. What originally inspired the development of the Quagi antenna was the need for a low-cost, high-gain antenna for moonbounce communications. Some of the commercial antennas then available fell far short of their advertised gain figures, especially at 432 MHz. After a series of attempts to improve the performance of one particular commercial 11-element Yagi, attention was focused on the driven element--which had an especially inefficient gamma match. On a hunch, the driven element was removed and replaced with a quad-style loop. The forward gain immediately increased from 6.4 dBd. to 9.8 dBd--a dramatic improvement for an antenna rated by the manufacturer at 13 dBd. That led to exhaustive efforts to optimize this hybrid antenna, working originally at 222 MHz. After many experiments, it was determined that Yagi-style directors delivered better gain than quad loops when the antenna was extended beyond four or five elements. But the use of a quad-style driven element and reflector offered several advantages, including good gain, good immunity to noise resulting from static buildup, and extreme ease of construction and impedance matching. After many designs were tried and rejected, the classic 8-element and 15-element designs were selected for publication. Later additional designs for 1296 were developed.

## Slide 4
Antenna range methodology
In this era of computer-optimized antenna designs, many radio amateurs are amazed that anyone would actually set up a home antenna range and perform the tedious job of designing an antenna one element at a time. Computer modeling has revolutionized the way radio amateurs look at antennas. Armed with one of the powerful software packages that have come along in recent years, it is possible to design more antennas in a day than could be designed in a lifetime on an antenna range. Consequently, actual field measurement of antennas--using the classic scientific method of experimental research--has gone out of fashion. However, computer modeling has its limitations. It is not always possible to model all of the variables that come into play with real-world antennas. And the modeling process has pitfalls even for the experts. Well-known software producer Brian Beezley, K6STI, published an article in Vol. 4 of the ARRL Antenna Compendium called "An Adventure in Antenna Modeling," in which he described his own frustrating attempt to design an antenna with exceptional low-angle radiation. Concluding, he said this: "In the end I decided to write up this fiasco for several reasons. First, I wanted to demonstrate how foolish it's possible to become when you get carried away with computer modeling. Powerful software is no substitute for common sense. Second, I wanted to point out how easy it is to draw invalid conclusions when you ignore the limitations of antenna-modeling algorithms."

## Slide 5
Roy Lewallen, W7EL, another well-known modeling software author, said much the same thing in a February, 1991, QST article, "MININEC: The Other Edge of the Sword." He cited an example of an amateur whose computer modeling showed that a dipole less than a foot above a poor ground yielded 45 decibels gain over a dipole. Of that amateur, Lewallen said, "...he recognized that the answer was ridiculous, but sometimes we're not so lucky and the errors are tougher to spot. Well then, how can a radio amateur who wants first-rate antenna performance be certain an antenna is really working as it should--or design a brand-new antenna?
One answer is to measure the antenna's gain against a known reference. Antenna gain measuring sessions have been conducted at VHF/UHF conferences since the 1950s. Often these sessions, in which antennas are sometimes measured side by side as shown in the 1977 photo at left, are conducted by antenna experts using professional quality signal sources and measuring instruments.

## Slide 6
But any amateur willing to invest some time can set up an antenna range somewhere and obtain accurate antenna gain measurements with nothing more sophisticated than a low-power transmitter, a receiver and an audio VU meter. I published an article in QST in October, 1977, called "Measuring Antenna Gain with Amateur Methods" to describe the procedures for doing this. Because so few amateurs do actual gain measurements today, it seems worthwhile to summarize what that article said here.
The article said that any clear area can be an antenna range. The trick is to avoid obstructions and reflections: if the received signal is louder when the antenna is pointed away from the source, there is a problem. To conduct comparison tests, two antennas are placed side by side on masts of the same height, using equal length feedlines. A steady signal (a carrier) is generated perhaps 40 wavelengths away, and it is detected on a CW/SSB receiver that is not overloaded but has its AGC disabled. Then a VU meter can be used to indicate the difference in received signal strength of the two antennas. As a precaution, the two antennas are swapped so that antenna #1 goes on the mast and uses the feedline formerly used by antenna #2. Given some care in measurements and a stable path, it is possible to determine the difference in the gain of the two antennas down to a fraction of a decibel.

## Slide 7
In the original Quagi development at 222 MHz, Will and I first started working with cubical quad-style loop elements until we were satisfied that we had loops that were performing as they should. Then we added elements, first using loops and then rod directors. We tried various lengths for each new element and adjusted the spacing for maximum gain. The addition of each new element, of course, required us to re-check the previous elements for length and spacing, monitoring the gain of the antenna during each change. After a lot of painstaking experimentation, we arrived at the designs for 144, 222 and 432 MHz that were eventually published. The 1296 antennas were designed five years later at N6NB's antenna farm in Woodland Hills, which was the forerunner of the Tehachapi Mountain antenna farm.

## Slide 8
Quagi construction notes for 144, 222 and 432 MHz
The original Quagi antennas used wooden booms (1x2 or 1x3 Douglas Fir, tapered at both ends to reduce the weight and wind load), but any other nonconductor (e.g., fiberglass, Plexiglas or even taped bamboo) can also be used. If an aluminum boom is used, the elements should be mounted on insulators above or below the boom (not passed through a metal boom). Many builders have used small pieces of hardwood molding to mount the directors atop an aluminum boom.
The driven element and reflector are mounted on nonconductive spreaders such as dowel rods or strips of Plexiglas to avoid interaction. The driven element has a coaxial connector (an SO-239 or type-N connector, which is preferable at UHF) at the center of the bottom side of the element and is fed directly with 50-Ohm coaxial cable. In the original design, covered solid #12 TW house wire was used for the quad-style elements. The use of other types of wire, or even removing the insulation, may change the resonant frequency enough that the length has to be adjusted.

## Slide 9
Suggestion: build the antenna to the dimensions shown in the chart and run an SWR curve, noting the SWR above and below the desired operating frequency. If it is lowest below the desired frequency, the driven element should be made shorter--or longer if the SWR is lowest above the desired frequency. The reflector should then be adjusted in length a similar amount. Many builders have used THHN wire, which is more readily available than type TW now. They generally report that the resonant frequency is higher than expected, which means the loop elements have to be lengthened slightly for THHN wire. Tests in 2003 indicated that each wire loop should be about one percent longer than the original dimension if THHN wire is used. Fine-tuning of the element length is usually not needed for the directors, provided they are made of 1/8-inch aluminum rods, brass welding rods or something similar--as long as the boom is a nonconductor or the elements are mounted on insulators above or below the boom. If the elements pass through a metal boom (even with insulating sleeves), the length will have to be adjusted experimentally (have fun!). The director lengths are tapered from longest (closest to the driven element) to shortest (at the front of the antenna).
Although the quad loops are square or circular, the antenna is linear in polarization, not circular. If it is fed at the bottom, the antenna will be horizontally polarized. Feed the antenna on either side for vertical polarization (and then mount the directors vertically, not horizontally.

## Slide 10
Some builders have tried baluns to correct the imbalance in this quad-style feed arrangement. In many cases, a balun introduces losses so great that it's better to live with the unbalanced feed than to try to correct it. Feedline radiation can be reduced by placing toroids on the feedline at the antenna. Also, the feedline should run away from the feedpoint along the boom or below it--and then down the supporting mast perpendicularly to the elements to avoid interaction problems. A phasing harness is needed if two or more Quagi antennas are stacked for additional gain. The simplest way to feed multiple bays is with a commercial power divider and equal-length 50-ohm feedlines from the power divider to each antenna. An alternative method is to feed each pair of antennas with odd quarter-wavelength multiples of 75-ohm coaxial cable going to a T connector and with 50-ohm cable from that point to the station. Most amateur radio reference books describe phasing harnesses more fully.
With a little practice, these antennas can be mass-produced in large quantities at low cost. I have built as many as 16 of them for e.m.e. work in less than a day.

## Slide 11
Original Quagi dimensions (from April, 1977 QST)

## Slide 12
Here is Will Anderson, then WB6RIV, with a modern HF-VHF-UHF station, circa 1972. How much of this equipment can you identify?
Some of the obviously homebrewed equipment includes (top left to right) an HF kilowatt amplifier, a two-meter 4CX250B amplifier, and a high voltage power supply. Directly below that there is a 500-watt amplitude-modulated 222 MHz rig that Will used for years as net control of the "220 Rag and Tech Net" on Sunday nights. Not shown is a 50 MHz amplifer that used a pair of 3-500z tubes (almost identical in appearance to the HF kilowatt). Below the HF kilowatt and two antenna rotor controls is a stripline 144 MHz kilowatt using push-pull 4CX250B tubes. To its right is a 28-to-50-MHz transverter using parallel 6146s in the final. The Heathkit SB-200 amplifier to the right of the transverter had been converted for six meters. To its right is the plate modulator for the 222 MHz rig. On the bottom shelf there is a Drake TR-3 HF transceiver, a Swan TV-2 transverter for two meters, a Drake TR-6 for six meters and a Hallicrafters HF receiver. A surprising amount of this equipment still works 40-50 years after it was built!

## Slide 13
Notes concerning the 1296 MHz antenna design
At 1296 MHz, even small variations in the dimensions can have a dramatic effect on the antenna's performance. In the original design, the reflector loop was overlapped by 1/8 inch and soldered together after being fitted through holes drilled in a plexiglas "spreader" mounted on the boom. The driven element loop was soldered to a standard UG-290 chassis-mount BNC connector. One end of the 9.25-inch loop was pushed as far as it would go into the center pin and soldered. Then the loop was shaped and threaded through a plexiglas spreader. Finally, the other end was fed into one of the four mounting holes on the BNC connector and soldered. In most cases, the best VSWR was obtained if the end of the wire just passed through the hole so that it was flush with the opposite side of the connector. These lengths can be optimized if a reflected power meter that works at 1296 MHz is available: the length of the driven element can be adjusted slightly for lowest reflected power. If a major change has to be made, the reflector should be adjusted a comparable amount. The loop elements were shaped into a square; the exact shape did not appear to be critical. The directors were made as follows. Using 1/16-inch brass welding rod, one director was cut just slightly shorter than four inches and then filed down as needed. Then another was cut and filed to the shortest dimension, as well as that could be determined with a good ruler. Finally, all of the intermediate elements were filed so that they tapered evenly in length from the longest (3.91 inches) to the shortest (3.59 inches in the case of the 15-element model). This information concerning the 1296 Quagi first appeared in the August, 1981, issue of QST.

## Slide 14
Dimensions of 1296 MHz Quagi antennas

## Slide 15
Performance? Quagi antennas have been measured for gain at VHF conferences many times. If well built, the 8-element model usually comes in between 12 and 13 dBd. forward gain over a dipole, while the 15-element model is around 14-15 dBd. gain. These antennas have been used by a number of record-setting VHF-UHF contest stations, sometimes in portable applications like the one shown in the photo here. This photo, taken in 1976 at Utah Pass, Utah shows an installation of six Quagi antennas (two each for 144, 222 and 432 MHz) plus a Yagi for 50 MHz. They are mounted on the original "Cabover Kilowatt" contest truck, which was featured on the cover of QST in August, 1971

## Slide 16
Once the experimenter has confidence in the integrity of the antenna range, it's quite possible to dispense with the receiver and VU meter and use a signal source plus a field strength meter such as the one shown in the photo at right (which also shows an assortment of elements of varying lengths, including one mounted on a meter stick for use in antenna design work).
Incidentally, although this test setup is most practical with VHF/UHF antennas, the same principles work at HF as well if one can obtain the right hardware (e.g., a tower trailer to support a reference antenna beside each antenna being tested). Also, new antennas can be designed using these antenna range principles. A variety of element length and spacing combinations can be tried until the best results are achieved. While this is far more tedious than computer modeling, it does produce repeatable, practical real-world results. The Quagi antenna was designed in this fashion in 1972.

## Slide 17: The W5UN 2 Meter QUAGI 97 The W5UN Quagi 97 is a computer optimized quagi derived from the original W5UN Quagi of the early 1980s. The length of the 1997 model has been deliberately shortened to allow it fit on a 24 foot boom. Performance is substantially higher than that of the original antenna. It now compares favorably with yagis of the same length. The two programs used to optimize the updated antenna were AO6 and NEC 2. This antenna has not been verified by actual construction. Gain and front to back will be as stated below. The only component of the antenna that needs verification is the 50 ohm match. Who would like to be the FIRST to build the actual prototype model?? Full consultation will be available to the prototype builder during construction. Contact w5un@wt.net if you wish to be the first! Antenna Characteristics: 23' 9" 11 Element Gain: 13.56 dBd at 144.100 Mhz F/B : 23 dB Stacking: Optimum: E Plane: 13.73' Optimum: H Plane: 12.86' Stacking can be reduced up to 90 percent of optimum and still achieve acceptable stacking gain. Optimum stacking is recommended, however. http://www.iw5edi.com/ham-radio/?the-w5un-2-meter-quagi-97,85

## Slide 18: W5UN QUAGI 97 Dimensions in FREE SPACE: Element Boom Pos. El. Length Material Reflector 0.0000" 84.37" loop. #12 solid INSULATED copper wire * Driven 16.2500" 82.43" loop. #12 solid INSULATED copper wire * Dir 1 37.1875" 36.168" 3/16" aluminum rod Dir 2 70.1875" 36.052" 3/16" aluminum rod Dir 3 102.5000" 35.817" 3/16" aluminum rod Dir 4 135.8125" 35.475" 3/16" aluminum rod Dir 5 169.0625" 35.179" 3/16" aluminum rod Dir 6 202.8125" 35.090" 3/16" aluminum rod Dir 7 234.2500" 35.324" 3/16" aluminum rod Dir 8 264.8750" 35.617" 3/16" aluminum rod Dir 9 285.0000" 35.108" 3/16" aluminum rod * #12 TW insulated solid copper wire is common house wire, found at most hardware and building supply stores. Do not strip the insulation. The above dimensions may be used for non-metallic booms like wood or fiberglass.
Notes: W5UN

## Slide 19: If you wish to use a metal boom with through the boom insulated elements, please apply the following correction to the directors only. The reflector and driven quad elements must remain insulated from the boom. Boom Diameter Correction Add 0.750" or 19.050MM 10.56% .0792" or 2.02MM 0.875" or 22.225MM 12.14% .1062" or 2.70MM 1.000" or 25.400MM 13.66% .1366" or 3.47MM 1.125 or 28.575MM 15.13% .1702" or 4.32MM 1.250" or 31.750MM 16.54% .2068" or 5.25MM 1.375" or 34.925MM 17.90% .2462" or 6.25MM 1.500" or 38.100MM 19.21% .2882" or 7.32MM 1.750" or 44.450MM 21.67% .3792" or 9.63MM 2.000" or 50.800MM 23.91% .4783" or 12.15MM
Notes: W5UN

## Slide 20: Further information concerning use of metallic booms with insulated 'thru-the boom' mounted elements follows: PROVEN ACCURATE FOR BOOM DIAMETERS SMALLER THAN .055 WAVELENGTHS. MEASUREMENTS BY DL6WU .FORMULA BY G3SEK. FORMULA: C = 12.5975B - 114.5B^2 C = CORRECTION FACTOR AS A FRACTION OF THE BOOM DIA. B = BOOM DIA IN WAVELENGTHS B^2 MEANS B SQUARED 2 METERS BOOM DIAMETER CORRECTION ADD 2 METERS. 2 METERS BOOM DIAMETER CORRECTION ADD 2 METERS. 0.750" OR 19.050MM 10.56% .0792" OR 2.02MM 0.875" OR 22.225MM 12.14% .1062" OR 2.70MM 1.000" OR 25.400MM 13.66% .1366" OR 3.47MM 1.125 OR 28.575MM 15.13% .1702" OR 4.32MM 1.250" OR 31.750MM 16.54% .2068" OR 5.25MM 1.375" OR 34.925MM 17.90% .2462 OR 6.25MM 1.500" OR 38.100MM 19.21% .2882" OR 7.32MM 1.750" OR 44.450MM 21.67% .3792 OR 9.63MM 2.000" OR 50.800MM 23.91% .4783" OR 12.15MM 20.000MM 11.04% 2.21MM 28.000MM 14.87% 4.16MM 30.000MM 15.78% 4.73MM 32.000MM 16.66% 5.33MM 38.000MM 19.17% 7.29MM Insulators can be commercial shoulder insulators and keepers or as simple as heat shrink tubing with the element held in place by hot melt glue or epoxy glue.
Notes: W5UN

## Slide 21: A look at some Quagi’s that I have built and used

## Slide 22: Quagi’s built and used
2M 15 element (16.5dBi) 28’ boom
Notes: 2m quagi

## Slide 23: 222 20 elm Quagi bottom (17.5 dBi 27’ boom) 23 elm M2 Long-John top (18.8 dBi 32.5’ boom)
Notes: 222 quagi

## Slide 24: 432 35 elm Quagi bottom (19.8 dBi 28’ boom) 27 elm M2 Long-John top (19.4dBi) 21’ boom)
Notes: 432 quagi

## Slide 25: What antenna I use at home

## Slide 26: 15 elm 2M Quagi (16.5dBi 28’ boom)
Notes: 15 elm Quagi @ home

## Slide 27: 18 elm 222 Quagi (17.4 dBi 23.5’ boom)

## Slide 28: Building a 15 elm Quagi
Notes: 15 elm quagi build

## Slide 29
Notes: 15 elm quai build

## Slide 30: 15 elm Quagi 4 Oct 2007
Notes: 15 elm quagi finished

## Slide 31: 15 element Quagi vs 15 element Yagi (16.5dBi) 28’ boom
Notes: vs

## Slide 32: Building a 15 elm Yagi fall 2018
Notes: 15 elm yagi

## Slide 33: Building a 15 elm Yagi fall 2018
Notes: 15 elm yagi

## Slide 34: In the air Oct 2018
Notes: Quagi & yagi

## Slide 35: 15 element Quagi and Yagi director length - same for both antennas spacing - same for both antennas height of element above boom-same for both antennas *difference – Reflector and driven element* Boom length – 28’ Gain @ 144.2 – 16.5 F/B – 22.4
Notes: Basic info on the 2 beams

## Slide 36: comparison notes
10 Oct – Dec 2018
Notes: Notes 1 10 Oct – Dec 2018

## Slide 37: comparison notes
10 Oct – Dec 2018
Notes: Notes 2 10 Oct – Dec 2018

## Slide 38: Build a Quagi for: Roving or Portable operating or Home (limited space) and/or (EME) See my paper
Notes: Options for building