## Slide 1: Observations on FM Contesting. Preparing to win and lessons from losing.
John Young, KM4KMU

## Slide 2: Topics
What does it take to do well?
2 Strategies & a common theme
3 Case Studies
Preparing to win
Lessons Learned from Losing

## Slide 3: FM Category
Lowest bar for entry of all VHF/UHF contest classes
  A great on ramp for new Technicians to be introduced to contesting
  Slow paced, almost conversational, a fun weekend on the radio
Very few entrants, ~20 logs submitted each contest
  Many ARRL divisions and sections get no entrants
QSO’s are local, 90% are under 100 miles
  It’s a “local” event
  Few if any will know there is a contest going on
  Often need to explain the exchange, give people their grid
A second or third place national finish is achievable with a little planning, coordination and effort.
Lets set some goals

## Slide 4: Analysis of QSO’s (40-60 )
Grid corner 2 band station top 3 finish: 45 contacts.
30 stations on 2m, QSY half of them (15) to 70cm for 45 contacts.
  30 pts on 2m+ 15x2pts 70 cm = 60 QSO pts.
FM simplex can be a desert: Let people know your on the air
Chart: QSO’s Top 3 in FM Average QSO’: 1st 117, 2nd 61, 3rd 45 Median since 2016 is 1st 144, 2nd 51, 3rd 41
| Jan 13 | June 13 | Sep 13 | Jan 14 | June 14 | Sept 14 | Jan 15 | June 15 | Sept 15 | Jan 16 | June 16 | Sept 16 | Jan 17 | June 17 | Sept 17 | Jan 18 | June 18 | Sept 18
1st | 59 | 23 | 34 | 87 | 54 | 64 | 103 | 114 | 103 | 181 | 176 | 144 | 202 | 144 | 129 | 156 | 70 | 259
2nd | 63 | 22 | 10 | 45 | 36 | 18 | 61 | 93 | 23 | 103 | 57 | 40 | 154 | 51 | 33 | 190 | 26 | 64
3rd | 21 | 15 | 11 | 18 | 34 | 25 | 91 | 47 | 18 | 88 | 30 | 41 | 90 | 40 | 28 | 119 | 44 | 58
Pre Contest Coordination is Essential: Get 30 club members on the air

## Slide 5: Analysis of Multipliers (10-15)
10 to 15 multipliers needed for a top 3 finish
  2 band station at a low altitude grid corner gets an easy 8 multi’s.
  Set up on a North-South Grid line 10-30 miles from the grid corner
  Rover tracking or a grid corner at altitude gets 3 or 4 more.
The big multiplier scores require a mountain top and 4 bands
Chart: Multipliers Top 3 in FM Average: 1st 23, 2nd 14, 3rd 10 Median since 2016: 1st 30, 2nd 15, 3rd 10
| Jan 13 | June 13 | Sep 13 | Jan 14 | June 14 | Sept 14 | Jan 15 | June 15 | Sept 15 | Jan 16 | June 16 | Sept 16 | Jan 17 | June 17 | Sept 17 | Jan 18 | June 18 | Sept 18
1st | 15 | 12 | 16 | 14 | 22 | 13 | 22 | 25 | 21 | 23 | 32 | 21 | 22 | 30 | 39 | 36 | 15 | 42
2nd | 7 | 12 | 5 | 4 | 11 | 9 | 24 | 28 | 9 | 12 | 15 | 15 | 31 | 15 | 11 | 20 | 11 | 10
3rd | 12 | 11 | 4 | 6 | 10 | 7 | 15 | 19 | 9 | 7 | 10 | 10 | 16 | 7 | 11 | 16 | 4 | 11
Mtn
top
Mtn
top
Mtn
top
Mtn
top
SOTA
Mtn
top
Mtn
top
Mtn
top
SOTA
Grid
Cnr
Mtn
top
SOTA
Grid
Cnr

## Slide 6: Analysis of Scores
2 Bands at grid corner: 11 Multi’s , 60 QSO points (660 score) 3rd place, maybe 2nd.
3 Bands on a grid corner: 15 Multi’s, 60 QSO points (900 score) 2nd place.
The lowest scoring contest (2nd & 3rd) is June.
Chart: Scores Top 3 Average: 1st 4166, 2nd 1458, 3rd 763 Median since 2016: 1st 6292, 2nd 1125, 3rd 462 Notice that 3rd place scores have been pretty flat recently
| Jan 13 | June 13 | Sep 13 | Jan 14 | June 14 | Sept 14 | Jan 15 | June 15 | Sept 15 | Jan 16 | June 16 | Sept 16 | Jan 17 | June 17 | Sept 17 | Jan 18 | June 18 | Sept 18
1st | 1080 | 360 | 688 | 1218 | 1650 | 1157 | 3080 | 3725 | 2835 | 5842 | 6976 | 4221 | 6292 | 5370 | 6669 | 8172 | 1500 | 14154
2nd | 441 | 321 | 75 | 232 | 616 | 243 | 2136 | 3612 | 306 | 1500 | 1215 | 855 | 6231 | 1125 | 506 | 5520 | 396 | 920
3rd | 324 | 242 | 56 | 189 | 510 | 224 | 1935 | 1425 | 189 | 924 | 430 | 530 | 2098 | 406 | 462 | 2704 | 244 | 847
Mtn
top
Mtn
top
Mtn
top
Mtn
top
SOTA
Mtn
top
Mtn
top
SOTA
Grid
Cnr
Mtn
top
SOTA
Grid
Cnr
Grid
Cnr
Pre Contest Coordination is Essential

## Slide 7: Example Analysis of FM Multiplier Goals: 2 Bands Range 2M (125mi) & 70cm (70mi) from 4,200’ ASL
Flagpole Knob 70cm Grids
Five at High Confidence
FM 07,08, 09, 18, 19
Four at Low Confidence
EM99, 98, 97 & FM 17
Flagpole Knob 2 Meter Grids
Eleven at High Confidence
FM 06, 07, 08, 09, 17, 18, 19
EM 97, 98, 99, FN00
Four at Low Confidence
FM16, FN10, EN90, EM96
Use Google Earth to plot elevation profiles to population centers and rover stops
Use the Pasternack Link Margin Calculator to estimate range. Assume a 3dB omni, 25W & 3dB losses for the other station.
Notes: Analyzed and visited 7 locations
Flag Pole Knob was the easy winner
11 two meter grids with high confidence
5 seventy centimeter grids with high confidence
There were several major population centers in easy range and I could work mobiles on I-81.
This is going to be way too easy!!!!

## Slide 8: 2 Strategies & a Common Theme
#1 Location Near a Grid Corner with Population
  Set up near a grid corner on a N-S grid line near population center
  Pre contest coordination with local club(s) & previous contacts
    This is the recipe for W2EV’s consistent success.
  Track the rovers. You may be low altitude but they ARE NOT. Extra Multi’s.
    “FM Rovers”. Friends taking the XYL out for scenic drive (into grids you need)
#2 Get Altitude
  If near a grid corner all the better. (KK4SOG)
  Remote mountain tops are worthless for FM.
    You need population within your demonstrated Tx & Rx range to omni’s @ 35w
    Let people know where you are. Nobody in Colorado does well in FM.
A Common Theme: Pre Contest Coordination
  FM Simplex can be a real desert. Every contact is golden.
  25 to 35 contacts is all you need for a top 3 finish (don’t forget to QSY)
  Get your club active on FM. Everyone has it.
  Few know there is a VHF/UHF contest going on unless you tell them.
Pre Contest Coordination is Essential

## Slide 9: 3 Case Studies
W2EV:
  The perennial winner (Rochester VHF/UHF club)
KK4OSG (now WG4I)
  “The Iron Ham”
KM4KMU
  Mad Max’s Shrimp Boat
Pre Contest Coordination is Essential

## Slide 10: W2EV (QTH Station): 7-1st and 3-2nd Places
Geography: 10 miles from a Grid Corner at 650 feet. Flat terrain.
Antenna’s: Omni’s all four bands
  Loads a 10m vertical for 6m.
Station: QTH
Coordination: Rochester VHF UHF club
  Sponsors a Rover Blitz. 6-10 rovers.
  Pre-runs contest to verify rover location
  effectiveness. Checks QTH to QTH paths and Rover to QTH paths.
  Passes out HT’s for FM roving and hill topping to new hams.
No one does pre-contest planning and coordination better than Rochester VHF/UHF
Study their news letters and web site
(Pacific North West VHF Society does a pretty darn good job too. Keep and eye on them)

## Slide 11: KK4OSG (WG4I) FM “SOTA” Station: 3-first place finishes
Geography: 4,660 ft. Blood Mountain
  20 miles from a grid corner,
  70 miles from Atlanta
Antenna’s
  Roll up j-pole 220 , dipole 6m,
  5-ele Elk dual band Yagi 2m/70cm.
  Push up mast.
Station: SOTA. 60 lbs including batteries.
  Packs everything in. Batteries are a big deal.
  Hand logs (Golden Logs, must be nice!!)
  FT-8900 + borrowed 220 rig.
Coordination: Supportive club and friends.
  Does not go to the extremes of the other 3 examples.
EM84
EM83
EM73
EM85
EM75
EM86
EM74
EM76
Altitude + grid corner + Population: 6 Line of sight grids
Good propagation: Reaches from SW Florida to Boston
Held record high score 2016-2018
25-32 Multi’s
140-180 contacts
It snows in Georgia

## Slide 12: KM4KMU Temporary High Altitude Fixed Site
Geography: 4,400 ft. Reddish Knob. Center of grid FM08JL
  Inside National Radio Quiet Zone. Zero squelch tolerable, zero QRM
  180 mile to 250 mile contacts are common. Best is 301 miles.
  80% of contacts are rural in Shenandoah Valley under 100miles.
Antenna’s:
  12 foot boom beams all bands. 45 Deg polarization.
  45 deg pol to work H pol “big guns” at long range.
Station: “Expedition” fixed site
  100W all bands. Mast mounted pre-amp on 70cm.
Coordination:
  Emails all previous contacts requesting a QSO.
  List gets longer every year, currently ~300 hams
Station built to chase grids/multipliers from FM08JL
Never wins January due to either weather or stupid mistakes
32-42 Multi’s
145-260 contacts

## Slide 13: Preparing to Win

## Slide 14: Doing Well: A top 3 finish
Get near a grid corner & population center (10-40 miles)
  Use Omnis as your primary antenna near a grid corner. Easy QSY
  Save the beams for working more distant grids
Coordinate with your club members
  One FM mobile (rover) circling your corner and going to high spots in other grids can get you all the multipliers you need.
  Use Google Earth to lay out lines of sight & Pasternack for link margins
Track the rovers to get grids beyond the grid corner.
Having 3 bands is a huge help
  I prefer 223.5 over 6m, 2pt QSO’s, very quiet, propagates better, smaller antenna
  Low cost at ham fests or you can borrow one from a club member.
Mount topping is not required but it is desirable.
Precontest Coordination is Essential: Otherwise simplex can be a desert

## Slide 15: Lessons Learned From Losing

## Slide 16: Lessons Learned From Losing
Log all your contacts.
  Even if they are not submitting logs they will count.
  11th vs 4th Jan 2016
Hand Logging?
  Take the time to write clearly. Don’t loose a log sheet.
  2nd vs 1st Jan 2017 (lost to W2EV by 1%)
Recon your site. Check for Noise
  Used a popular June-Sept Rover site (ski resort) January 2018
  S-7 noise from lift motors, car ignitions and LED flood lights
  I was QRT in 9 hours. Everyone heard me, I heard very very few.
Keep It Simple Stupid
  Minimize nuts, bolts, tools, set up time (practice)

## Slide 17: Lessons Learned From Losing (Jan 2019)
Always bring Omnis When working populated grid corners
  Tried to work a heavily populated grid corner January 2019 using beams from 2,500ft ASL
  A copy of W2EV’s set up but I brought beams not omni’s (BIG MISTAKE)
  Massive turn out. Huge pile ups on 146.520. FM mobiles everywhere.
  Impossible to QSY everyone. Lost 2/3rds of my 2m contacts on the QSY to 70cm.
Always bring Omnis When Ice Threatens
  Beams iced up in 3 hours and I went QRT.
  I did not bring any easy to de-ice omni’s.
  1,300 pts in 3 hrs is not bad but I could have
  stayed on the air with omni’s.
You learn more by losing.
CQB with a Barrett .50. Antenna firepower was a disadvantage
I should have brought mag mount whips, easy to QSY, easy to de-ice
Working a Grid Corner? Use Omni’s!!
Ice really screws up the VSWR

## Slide 18: Lessons Learned From Losing
Mark a road Atlas with grids 300 miles all directions.
  On FM many people don’t know their grid squares.
  You need to give people their grid squares.
  Butt In Chair. 2nd place vs 1st January 2017
  I abandoned my mountain top site when ice started forming.
  I was weak. I wanted a hotel room instead of a tent.
  16 hrs on air over 2 days. I lost by 61 pts.
  10 more minutes on the air would have given me first place.

## Slide 19: What is Unique About FM?
Coordination is ESSENTIAL to get people on the air.
  More important on short range FM than SSB.
  Clubs, repeaters, emails. Get the word out
FM is more “genteel”
  Slower paced than SSB, few if any contesters. You can give them Mike Fright.
Be polite, be interesting, relax & laugh a little, create a pile up
  You’re on their turf, disrupting their daily routine. Make it fun for them, you are unique!
  Do a couple of rounds. Your station is cool, they are curious, be conversational
  There are many listening, they will call if you make it fun.
  Hams will jump in mobiles to give you new grids & higher bands if they like you
Be Patient
  Explain contesting, explain the exchange, be ready to give them their grid.
Don’t hammer the calling freq with “CQ Contest” every 10 seconds
Be honey not vinegar You will get some pile ups
Notes: Altitude, antenna gain, power. No rocket science here.
FM simplex is where friends meet friends. Be a friend.
Be patient. Ask about their station, describe yours. Talk for a round or two.
You and your station are fascinating exotic creatures on FM!
Be ready to explain the exchange and give people their grid square.
Every tech has VHF/UHF. Thirty thousand new contest capable amateurs each year.
Work with your club to get them on the air

## Slide 20: A challenge to YOU Get 1 Technician on the Air in June

## Slide 21: Questions?
Answers !
Credits:
W4IY: Woodbridge Wireless Contest Group
K8GP/R: Terry & Andy
K2EZ/R: Andrea
KW4EP: Jacek & his magic spectrum analyzer
Chaos Fab Shop: AK & Vince
Most importantly
The XYL, Jo