## Slide 1: Feeding and Phasing A Practical Look at Feeding and Phasing the Latest LFA Antennas for the 2M VHF Band
Al Rabassa, NW2M
VHF Super Conference
April 26-28, 2019
Sterling, VA

## Slide 2: Today’s Topics
Introduction to Phasing Principles
Common Phasing Examples
Basic Formulas, Terminology, Units
Introduction to Splitters/Combiners
Using Coax Cable as a Phasing Harness
Checking Your Work using a VNA
Summary / Wrap-up / Q&A

## Slide 3: Phasing Basics: Goal
Combine 2 or More Antennas
Achieve the Magical +3dB Gain
Signals Must Arrive In-Phase
Impedance Must be 50Ω in/out
Frequency (Band) Dependent
Minimize Losses / Diminishing Returns

## Slide 4: Most Common RF Phasing?
You Saw 20-30 on Your Way Here-
Co-Phase Two CB Antennas
Antennas are 9’ Apart (1/4
Harness is 12’ Long, 75Ω
246 / 27 * 2 * 0.66 * 1 = 12 Feet

## Slide 5: Formulas / Terms / Units
246/fMHz = ¼Wavelength Free Space (ft)
VF – Velocity Factor, Speed in Coax, <1.0
Units of Measure: Feet/Inches, VF%
1° Cutting Err (0.66VF): 2M(0.25”),11M(0.8”)
Odd Multiples (1, 3, 5, … 17, …)
Example:
    246 / 27 * 2 * 0.66 * 1 = 12.02 Feet (144”)
    246/144 * 2 * 0.66 * 1 = 2.25 Feet (27”)
Common Mode Current

## Slide 6: Transmission Line Impedance

## Slide 7: Splitters / Combiners

## Slide 8: 2M Stack LFA2M-12EL
Loop Fed Array Antenna
Commercial Product
Computer Modeled
Direct 50Ω Feedpoint, Balanced Feed
RF Choke for CMC

## Slide 9: Phasing Harness Length
Stacking Distance: 12’
Rear Boom Length: 10.5’
Feedpoint Loop: 2’
6’ + 10.5’ + 2’ = 18.5’
18.5’ ÷ 1.1275’ = 16.4x
Next Odd Integer = 17x
(246/144 * 0.66 * 17) = 19.17’ = 230”

## Slide 10: Building the Harness
Terminate 20’ with N-Connector (240”)
Using VNA, Sweep Coax (144 MHz Focus)
Trim Until 144.000 MHz Null Reached
Cut Coax to Make 1.5” Pigtails
Re-Sweep Using VNA, 144.400
Make Second Harness Leg
Result: A Matched Pair
Attach Ferrites & HST

## Slide 11: Summary
Actual VF was 0.676 (2.4% error)
235.5” Measured vs 230” Calculated
VNA was Very Sensitive to Shield Length
VNA Insensitive to Pigtail Length
Harness Weight vs Static Balance, 12” Shift
Ferrites: 31 Mix, 0.5” ID x 1.125”, FB102-31
Glue-Infused 1” Heat Shrink Tubing
Result: Precision 2-Port Phasing Harness

## Slide 12: Q&A
Questions?
Hands-on Lab:
  I will be here with VNA and Tools
  Vendors Have Parts
  Come: Try, Test, Build, Tune
  Note: Any and all products, graphics, photos, and formulae mentioned are for reference and clarity proposes only. It does not constitute an endorsement, use, preference, advertisement, or suitability to task. This does not constitute direction or consulting advice. All products, product names, logos, or trademarks mentioned remain the sole ownership of their respective owners.
(unofficial)