## Slide 1: Visualing Microwaves
Paul Wade W1GHZ

## Slide 2: Visualizing Microwaves
Invisible to eye
Visible to RF detector
On transmission line
In Waveguide
In space

## Slide 3: Microwaves
Traveling at Speed of Light
Hard to see
= 23 cm

## Slide 4: Visualizing Microwaves
Stop the sine wave – Short circuit
Voltage must be ZERO at short circuit
Wave stands still – Standing wave

## Slide 5: Standing Waves on T-Line

## Slide 6: Open Coaxial Line Hobby Tubing Center and 4 ground lines

## Slide 7: Sensitive RF Detector ADL5513 from SV1AFN 21 millivolts per dB -50 dBm to -3 dBm

## Slide 8: RF Probe

## Slide 9: RF Probe & Detector

## Slide 10: Signal Source only a few milliwatts needed

## Slide 11: Probe Standing Waves

## Slide 12: Probe on Transmission Line
Sensitive detector – very low power level
  ~30 dBm max from probe
  Low radiation levels = SAFE
Indicators
  Bargraph
  Tonemeter
  Digital Voltmeter for accurate dBm difference

## Slide 13: Standing Wave Ratio
Probe voltage along line
Detector output in dB: 21 mV per dB
Convert dB difference to Voltage Ratio
Voltage symmetrical around coax

## Slide 14: Short Circuit
High VSWR
Vmax to Vmin ~27 dB (Noise Floor limited)
Voltage Ratio = VSWR >22
Minimum at 5.5 and 17 cm
Half-wavelength = 17 – 5.5 cm = 11.5 cm
1296 MHz -> 23 cm

## Slide 15: Open Circuit
High VSWR
Minimum at 12 and 23.5 cm
Half-wavelength = 23.5 – 12 cm = 11.5 cm
Minimum and Maximum position reversed from Short Circuit

## Slide 16: 50 ohm Termination
Low VSWR
Vmax to Vmin 3.3 dB
Voltage Ratio = VSWR = 1.5
Transmission Line Zo NOT 50 ohms
  Probably higher

## Slide 17: 100 ohm Termination
Low VSWR
Vmax to Vmin 8.6 dB
Voltage Ratio = VSWR = 2.7
Transmission Line Zo NOT 100 ohms
  Probably lower

## Slide 18: 68 ohm Termination
Low VSWR
Vmax to Vmin 3 dB
Voltage Ratio = VSWR = 1.4
Transmission Line Zo NOT 50 ohms
  But has 50 ohm SMA connectors
  Always some mismatch

## Slide 19: 68 ohm Termination

## Slide 20: Waveguide WR-229 at 3456 MHz

## Slide 21: Probing Waveguide
Waveguide = copper mesh
Mesh inside waveguide – slightly smaller
Slot in center of wide wall
Probe thru mesh for other locations
Same source and detector
Slightly longer probe

## Slide 22: Waveguide setup

## Slide 23: WR-229 Waveguide Short
High VSWR
Vmin at 8.5 and 17 cm
guide ~ 17 cm
o = 8.7 cm
guide > o

## Slide 24: Waveguide Open
Low VSWR
Open waveguide radiates as antenna
Polarized

## Slide 25: Radiation and Polarization

## Slide 26: Waveguide Terminated very low VSWR

## Slide 27: Probe across Waveguide probe thru mesh

## Slide 28: WR-187 Waveguide
Smaller guide very close to cutoff
Vmin spacing longer than slot
g >> o

## Slide 29: Summary
Open or mesh structures allow probing
Sensitive detector for electric fields
  Coax
  Waveguide
  Antennas
  Leakage
  Optical equivalents:
    Reflection, refraction, diffraction, polarization

## Slide 30: Heinrich Hertz 1887
Experiments included open coax
Spark gap source – high power
Spark gap detector – very insensitive
~ 50 MHz
Demonstrated optical equivalance:
Electromagnetic waves
MIT Museum Exhibit of replica apparatus

## Slide 31: www.w1ghz.org