## Slide 1: Design and development of a GPS Disciplined Oscillator
Mike Cresap, W3IP

## Slide 2: GPSDO – Time to update the transverters
LOs need more stability
LOs need more accuracy
Always want better phase noise
Shack is too cluttered already

## Slide 3: How do we “get on frequency” and stay there?
Something GPS based is the answer
Anything else seems to be a bandaid
  Try to rebuild your existing crystal oscillator or oven controller and figure out what is not in the book
  Calibrate (often) to an external beacon that you hope is really GPS locked

## Slide 4: GPSDOs - disciplined oscillators
PLL Synthesizer
Phase locked loop
GPS Receiver
Optional
Low Noise Oscillator

## Slide 5: GPSDO – what is it?
Best of both worlds
  Long term stability derived from the GPS cesium clocks
  Short term stability (phase noise) from high quality on board crystal oscillator

## Slide 6: GPSDO – a bit of history
Military uses –expensive boxes by companies like Symmetricom
Commercial uses – cell phone frequency standard – remember the Z3801 with its 6 channel GPS receiver?

## Slide 7: GPSDO – more recent history
New chip vendors
  UBLOX – small GPS receivers with integrated RF output
  Silicon Labs – clock oscillators and jitter attenuators
Leo Bodnar
SV1AFN

## Slide 8: GPSDOs – where are they applicable?
Local oscillators for transverters
Beacon transmitters
Reference oscillator for HF receivers, signal generators, spectrum analyzers
Weak signal sources

## Slide 9: GPSDOs – what’s new?
More independent channels
Lower phase noise
Latest generation components
SI5394 - 4 channels
Crystal filter following TCXO
Ublox M8 GPS receiver

## Slide 10: GPSDO – simple block diagram
GPS receiver
SI-5394 PLL + dividers
1575 MHz
10 MHz
4 outputs

## Slide 11: GPSDO – what should we expect?
* Results obtained using battery power source, USB results will be worse!
116 MHz | Wenzel | 116 XO | SI5394 | LB Mini* | DigiLO | VHF ApolLO
Phase noise Measurement | (FSWP) | (FSWP) | Datasheet | phase detector | Datasheet | Datasheet
100 Hz | -123.7 | -123.4 | -96.6 | -105.0 | -97 | -85.7
1 KHz | -152.7 | -149.7 | -123.6 | -122.0 | -112 | -104.7
10 KHz | -164.7 | -157.3 | -139.6 | -127.0 | -115 | -108.7
100 KHz | -167.7 | -163.5 | -147.6 |  | -120 | 

## Slide 12: GPSDO – real life
 | BEACON case |  |  |  | Contest station case 1 |  |  | Contest station case 2 | 
Frequency |  | 144.3 | Mhz |  | 144.3 | Mhz |  | 144.3 | Mhz
Transmit power (watts) | 10 | 40 | dBm | 1000 | 60 | dBm | 1000 | 60 | dBm
Cable loss |  | -1 | dB |  | -1 | dB |  | -1 | dB
Transmit antenna | halo | 1 | dBi | 12 el yagi | 14.5 | dBi | 12 el yagi | -6 | dBi
Effective radiated power |  | 40 | dBm |  | 73.5 | dBm |  | 53 | dBm
Path Loss (1.0 mile) |  | 79.8 | dB |  | 79.8 | dB |  | 79.8 | dB
Receive antenna |  | 10 | dB | 12 el yagi | 14.5 | dB | 12 el yagi | -6 | dB
Cable loss |  | -1 | dB |  | -1 | dB |  | -1 | dB
Carrier Power to receiver |  | -30.8 | dBm |  | 7.2 | dBm |  | -33.8 | dBm
100 Khz offset |  | -147 | dBc/Hz |  | -147 | dBc/Hz |  | -147 | dBc/Hz
100 KHz offset absolute |  | -177.8 | dBm/Hz |  | -139.8 | dBm/Hz |  | -180.8 | dBm/Hz
Receiver noise bandwidth |  | 500 | Hz |  | 500 | Hz |  | 500 | Hz
Receiver noise bandwidth |  | 27 | dB |  | 27 | dB |  | 27 | dB
Phase noise power at receiver |  | -150.8 | dBm |  | -112.8 | dBm |  | -153.8 | dBm
Receiving system noise floor 3 dB noise figure (500 Hz BW) |  | -144.0 | dBm |  | -144.0 | dBm |  | -144.0 | dBm

## Slide 13: GPSDO – not so simple block diagram
GPS receiver
SI-5394 PLL
1575 MHz
4 outputs
1.6 MHz BPF
50 MHz TCXO
50 MHz Xtal filter
3.3v regulator
3.3v post regulator
1.8v regulator
1.8v post regulator
USB ESD
USB micro-b
MSP430 micro
4-5 volt supply

## Slide 14: GPSDO – the build process
Design – block diagram
Design – circuit simulation
Design – schematic capture
PCB layout – 2 layer board
Express PCB
Express PCB
Power Point
QUCS

## Slide 15: GPSDO – the build process
Solder paste
Toaster oven

## Slide 16: GPSDO – the build process
Inspection
Mechanical

## Slide 17: GPSDO –Prototype 2
GPS antenna
USB connector
1.8 v regulator
3.3 v regulator
GPS rx
1-1000 MHz outputs
PLL
TCXO
Filter

## Slide 18: GPSDO setup – Digital Data Flow
Computer
PC
SI-5394 PLL
MSP430 micro
USB
I2C
GPS receiver
Clock Builder
uCenter

## Slide 19: GPSDO – Microprocessor selection
USB and I2C compatible
Must have factory bootloader
Small pin count
MSP430F 5xxx/6xxx
Lots of code
Eliminates the inexpensive PICs
Wishful thinking – 48LQFP
CCS code bloat

## Slide 20: GPSDO – Testing 1,2,3
Regulator – function
Regulator – performance
GPS receiver – function
GPS receiver - performance
Spectrum Lab
U-Center
SignalHound

## Slide 21: GPSDO – Testing 1,2,3
Clock multiplier – function
Clock output – levels
  +6.5 dBm typical
ClockBuilder Pro
SignalHound

## Slide 22: GPSDO – Phase noise testing
Oscillator #2
50 Hz -100KHz Output
50 Hz HPF
Low freq amplifier
Mixer
Oscillator
#1
50 Hz HPF
Assumptions
One oscillator much lower phase noise than the other
One oscillator can be adjusted to within a Hz or two of the other – and stay there

## Slide 23: GPSDO – Testing 1,2,3
100 MHz output – phase noise
Prototype-2 Phase noise performance
Spectrum Lab
100 MHz | Wenzel | W3IP | SI5394
Phase noise | (FSWP) | Phase det. | Datasheet
100 Hz | -125.0 | -97.8 | -97.9
1 KHz | -154.0 | -120.8 | -124.9
10 KHz | -166.0 | -135.8 | -140.9
100 KHz | -169.0 |  | -148.9

## Slide 24: GPSDO – PLL power consumption
VDD: | 1.8 V
Ta: | 70 °C
Airflow: | None
 | Frequency | Format | Voltage | Current | Power
VDD |  |  | 1.8 V | 187.3 mA | 337 mW
VDDA |  |  | 3.3 V | 117.4 mA | 387 mW
VDDO0 | 116 MHz | LVPECL | 3.3 V | 22.6 mA | 74 mW
VDDO1 | 192 MHz | LVPECL | 3.3 V | 23.1 mA | 76 mW
VDDO2 | 404 MHz | LVPECL | 3.3 V | 24.5 mA | 81 mW
VDDO3 | 100 MHz | LVPECL | 3.3 V | 22.5 mA | 74 mW
Total |  |  |  | 397.2 mA | 1.030 W
Assumptions
Total Power: 1.030 W, On Chip Power: 960 mW, Tj: 91 °C
Note:
On-chip power excludes power dissipated in external terminations.
Tj is junction temperature. Tj must be less than 125 °C (on Si5394 Revision A) for device to comply with datasheet specifications.
Total power includes on- and off-chip power. This is a typical value and estimate only.

## Slide 25: GPSDO – development boards
Crystal tester
BPF
LPF
GPS Rx
GPSDO prototype 1
GPSDO prototype 2

## Slide 26: GPSDO – Transverter Integration
VHF transverters
  Many mixers want +17 dBm
  Remove DC power from oscillator and oven (PTC)
  Feed GPSDO signal into driver amp, ac coupled

## Slide 27: GPSDO – Transverter Integration
Microwave transverters
  Multi PCB transverters – Disable the crystal oscillator and lower multiplier stages
  Feed GPSDO signal into multiplier on micowave board, ac coupled
LO

## Slide 28: GPSDO – Transverter Integration
Microwave transverters
  Single PCB transverters (DB6NT) – Analyze block diagram and schematic, find highest frequency in LO chain supported by the GPSDO
  Remove DC power from oscillator and lower level multipliers
  Feed GPSDO signal into next multiplier
AC coupled at 639 MHz

## Slide 29: 4 channel GPSDO – in the box

## Slide 30: GPSDO – Prototype-2 Datasheet
Number of channels: 4
Frequency range: 10-720, 734-800, 825-1028 MHz
Power output: 6.0 dBm minimum 1-500 MHz
2.3 dBm at 1024 MHz
Channel to channel Isolation: 50-85 dB
Phase noise at 100 MHz (clean power source)
  -98 dBc/Hz at 100 Hz
  -121 dBc/Hz at 1 KHz
  -136 dBc/Hz at 10 KHz
Size: 3.2 by 2.1 by .91 inches (excluding connectors)
Power consumption: 5 volts, .67 amps max

## Slide 31: GPSDO - Summary
Described the design process for a 4 channel GPSDO
  Evaluated existing hardware
  Identified areas for improvement
  Tested circuits in phases
  Developed circuit values, schematic, PCB, BoM, mechanical package
  Tested key parameters – channel to channel isolation, phase noise