## Slide 1: MAP65 Version 2
Joe Taylor, K1JT
Joint Mid-Atlantic and North East VHF Conference
October 13, 2012
A Panoramic, Polarization-Matching Receiver for JT65

## Slide 2: MAP65: What is it?
SDR software, works with JT65 signals
“Big brother” to WSJT
Rx hardware converts RF to baseband
Decodes all JT65 signals in 90 kHz BW
X-Pol: Automatic polarization matching
Designed for EME on 144, 432, 1296 MHz

## Slide 3: JT65 Protocol
60 s T/R sequences
Compact, structured messages
Modulation: 65-tone FSK, 2.7 baud
ECC: Reed-Solomon (63,12)6
Works at 10 to15 dB below CW limit
> 1000 EME users on 144 MHz !

## Slide 4: Program Comparison
WSJT
BW 2-5 kHz
Many modes
Decodes one signal
One polarization
MAP65
BW 90 kHz
JT65 only
Decodes all signals in passband
All polarizations (avg 3 dB better)
Automatic Band Map

## Slide 5
RF to Baseband
X
Linrad, SDR-Radio
(optional)
MAP65
Hardware
Software
Wide
Graph
Messages
Astro
Data
Main
Window
Band Map
Y
Notes: <number>

## Slide 6: MAP65: Version 2 Features
Supports X-pol and Single-pol systems
Sub-modes JT65A, B, and C
Sample rate: 96000 or 95238 Hz
Optional front-ends: Linrad, SDR-Radio
Rx hardware: WSE converters, IQ+, Perseus, SDR-IQ, FUNcube Dongle, SoftRock, …
QtSDK, C++ for GUI; Fortran for decoder
Windows, OS X, Linux, …

## Slide 7: Example Receivers

## Slide 8: SDR-Radio

## Slide 9: Normal Operation at K1JT (2m EME)
Turn on Rx, warm up PA
Start Linrad and MAP65
Click to track Moon
Callsigns start to appear on screen
Double-click on a CQing callsign
Select Tx polarization (H or V)
Click “Auto On” to call him

## Slide 10: MAP65: Full Screen Display

## Slide 11: Main Window
QSO Window
Tx Messages

## Slide 12: Wide Graph

## Slide 13: Wide Graph (detail)

## Slide 14: Band Map
2 × 10-element
Xpol Yagis

## Slide 15
Band Map
(grayscale)

## Slide 16: Messages

## Slide 17: Rx Hardware Interfacing
 | SoftRock | FUNcube Dongle | SDR-IQ, Perseus | SoftRock × 2 | IQ+ VL, V, U | WSE
Input Freq (MHz) | 28, 144 | 144, 432, 1296 | 28 | 28, 144 | 50, 144, 432 | 144
Polarizations | 1 | 1 | 1 | 2 | 2 | 2
Soundcard Channels | 2 | – | – | 4 | 4 | 4
Digital Interface | USB | USB | USB | USB | USB | Parallel Port
Frequency Control* | L, S, M | L, S, M | L, S | L, M | L, M | L
Front-End Software* | L or S optional | – | L or S required | L optional | L optional | L optional
* L = Linrad, S = SDR-Radio, M = MAP65

## Slide 18: MAP65: Why do you need it?
Random EME on 144, 432, 1296 (no skeds or logger)
Superb wideband noise blanker
Copy all EME signals in band
Monitor CW as well as JT65 portions of band
Powerful EME contest operating aid !

## Slide 19: Setup | Options – Station tab

## Slide 20: Setup | Options – I/O Devices

## Slide 21: Astronomical Data

## Slide 22: Station Control at K1JT
File azel.dat
13:01:28,211.3, 64.1,Moon
13:01:28, 98.3, 33.9,Sun
144, 162,Doppler
115,0,fQSO

## Slide 23: More Setup Features

## Slide 24: Setup Utility for FUNcube Dongle

## Slide 25: Online User’s Guide

## Slide 26: 432 and 1296 MHz
“Best” EME bands
Much smaller Tsys
Much smaller antennas are “enough”
Hear your own echoes with:
  432: 4 x 6m yagis, 250 W
  1296: 3m dish, 150 W
MAP65 is great for JT65 and CW !
Use Xpol Yagis on 432
Single pol’n (RHC/LHC) on 1296

## Slide 27: Possible Future Modes? JT65B2, JT65C2
2 × speed, for EME contesting
30 s T/R sequences  up to 20 QSOs per hour !
Sensitivity: 3 dB less
Presently available in WSJT (only)
Possible problems …
  QRM? Sub-band plan? Switching between modes?