## Slide 1: 10 GHz Preamp Simple & Cheap plus 5760 Preamp
Paul WaDE W1GHZ ©2025

## Slide 2: Simple and Cheap 10 GHZ Transverter needs a preamp (or LNA)
Good ones cost > $100
How about an OK one?
Can it be done for $10?
GOAL:
  NF ≤ 1.5 dB
  Easy to build
  Simple tuning
  You hear me better!

## Slide 3: Low Noise Device
CEL CE3512K2-C1
For Ku band LNB
0.3 dB NF at 12 GHz
Mouser
  $1.67
  26000 in stock

## Slide 4: Design Process
No fancy software
S-parameters
Plot on Smith Chart with Ansoft Designer SV
Guess at a transmission line circuit
Add T-lines
Plot again on Smith Chart
Fiddle and repeat
Draw T-lines on PCB layout

## Slide 5: Simple PC board
Ordinary PC board (cheap)
Thin – lower loss & radiation

## Slide 6: Several Trial Designs
All work, good gain, NF 2 to 3 dB

## Slide 7: Schematic

## Slide 8: Negative Bias Board
Uses Optoisolator to generate negative voltage
Shine light on an LED and it produces voltage
Same with a transistor
Optoisolator has LED lighting transistor
Transistor produces floating voltage
  About 0.4 volts at 50 microamps
  Enough to bias a GaAsFET
Circuit is fool-resistant
  Maximum voltage and current safe for FET
  Wrong connections also save

## Slide 9: Bias Board
Fool-resistant – Drain current powers optoisolator to produce negative bias

## Slide 10: About $2 in parts

## Slide 11: Fine Tuning - Snowflaking

## Slide 12: Three New Designs
WA1MBA W1GHZ Combo

## Slide 13: Simple Tuning – X-Acto knife

## Slide 14: With Bias Board

## Slide 15: SMA Connectors – Thin PC board 0.8mm SMA on 0.6mm board

## Slide 16: Robust Clamshell Housing Clamp SMA to reduce flexing

## Slide 17: Preamp Completed

## Slide 18: Alternative – Foil under SMA

## Slide 19: Foil Assembly

## Slide 20: Traditional Soldered Brass (Zack Lau W1VT)

## Slide 21: Blocking Capacitors - IN and OUT make a difference
Good 0603 chips work well, solder easily
  AVX (was ATC) S500 1.0 pf
  ~0.1 to 0.2 db better
  Fragile
  Hard-to-obtanium (sample kits?)
AVX (was ATC) S600 1pf – nearly as good
AVX (was ATC) S500 2.0 pf – nearly as good
  Modest quantity available

## Slide 22: Capacitors
AVX 600S 1.0pf AVX 500S 2.0pf AVX 500S 1.1 pf

## Slide 23: Noise Figure
HP 8970A
  12 Preamps read ~ 1.5 dB before tuning
  1.2 to 1.5 dB after tuning – simple stub trim
CS/G – cold sky to ground
  3 preamps measure 1.24 to 1.52 dB
  Slightly better than NF meter
Test by EB3FRN on Agilent E4407B
  Measured 1.50 dB vs my 1.30 dB

## Slide 24: System Noise Figure
Preamp with ≤ 1.5 dB NF, 12 to 13 dB gain
Simple and Cheap Transverter NF ~8dB
Together about 2 dB NF
Plus cable loss
Put the preamp at the feed

## Slide 25: Stability Test Antennas are not broadband terminations
Inject Noise Source thru 10 dB Coupler
NF 10 dB higher
Put SHORT and OPEN on Antenna port
No oscillation
Sliding short would be better test

## Slide 26: Maybe not $10
GaAsFET CE3512 (0.3 dB NF) $1.67
SMA Taoglass $3.50 x 2 $7
PC board $4
ATC capacitors $1 x 2 $2
Chip resistor and caps $0.50
Negative bias board & parts $2
=====
How about ~$15

## Slide 27: Summary – 10 GHz
Simple and Cheap 10 GHz Preamp
Good performance
Easy to build
Simple, repeatable tuning
PC boards available
Parts from Mouser

## Slide 28: 5760 Preamp or LNA

## Slide 29: 5760 MHz Preamp
Follow 10 GHz example
Same Device - should be better performance
Same Design Process – mostly snowflaking
Lower Cost
  0.8mm (1/32”) thick PC board – more common
  Cheap SMA connectors
  Ordinary 0805 capacitors (selected type)
Same bias board

## Slide 30: Tuned Prototype Three copies same tuning  artwork

## Slide 31: Schematic

## Slide 32: NO Tuning needed

## Slide 33: Same Bias Board as 10 GHz

## Slide 34: Robust Clamshell Housing

## Slide 35: Preamp Complete

## Slide 36: Stability Test

## Slide 37: Noise Figure
HP 8970A reads 0.7 to 1.2 dB
CS/G under 2 dB
  Hard to find Cold Sky
Better measurements at conference

## Slide 38: Summary
Good preamps for 10 GHz and 5760 MHz
Inexpensive
Easy to build
Parts & PC boards available
Simple Tuning
Fool-resistant negative bias circuit
Improved performance for Simple & Cheap Transverters