## Slide 1: Measuring VSWR or Return Loss at Microwaves
Paul Wade W1GHZ

## Slide 2: Microwaves
Traveling at Speed of Light
Hard to see
= 23 cm

## Slide 3: Visualizing Microwaves
Stop the sine wave – Short circuit
Voltage must be ZERO at short circuit
Wave stands still – Standing wave

## Slide 4: Standing Waves on T-Line

## Slide 5: Standing Wave Ratio
Measure voltage with moving probe on slotted line

## Slide 6: Return Loss
Return Loss = 10·log
Return Loss = |S11|

## Slide 7: Return Loss and VSWR Vector Network Analyzer
VSWR
S11
Return Loss = |S11|

## Slide 8: VSWR Return Loss & Reflected Power

## Slide 9: Realistic Return Loss
20 dB RL = 1% Power reflected – OK
  VSWR = 1.22
15 dB RL = 3% - not bad
  VSWR = 1.43
10 dB RL = 10% - usable
  VSWR = 1.92
< 10 dB - need to fix
> 20 dB - nice, but can we measure?

## Slide 10: 10 GHz and Up VNA
TinyVNA only to 6 GHz
10 GHz+ VNA
  Big, Heavy, and Expensive
  Big, Heavy, and Old
  Waveguide Calibration problematic

## Slide 11: Directional Coupler Measure Power in one direction
Reverse coupler for reflected power

## Slide 12: Directional Couplers

## Slide 13: Directivity
Directional Couplers are not perfect
Some reverse power leaks into forward measurement = error in POWER
Some forward power leaks into reverse measurement = error in Return Loss
Leakage can add or subtract – depends on phase
Directivity is magnitude of leakage

## Slide 14: Directivity & Error
Example:
Antenna Return Loss = 20 dB (1% reflected)
Coupler Directivity = 20 dB (1% leakage)
Coupler output can be between
  High = 1% + 1% RL =17 dB
  Low = 1% - 1% RL = 
Can you tune with this error?

## Slide 15: Coaxial Directional Couplers
Directivity 20 dB or less at 10 GHz
Coupling Factor

## Slide 16: Sensitive Detector Required
Coupled reflected power down by:
  Coupling factor - 10 to 30 dB
  + Return Loss – up to 40 dB
Need at least 50 dB below forward power
  -50 dBm at small signal level
  Test at high power?
Spectrum Analyzer
  TinySA Ultra not that sensitive
  Single frequency measurement
VNA

## Slide 17: Diode Detector
More sensitive than power meter
Measures peak voltage, not power
Not linear – relative readings
Sensitive to harmonic content in signal

## Slide 18: High Coupler Directivity for Accurate RL Measurement
Tools ->
Return Loss
Error
Calculator
Measured
VSWR=1.25
1.04
1.56
Actual VSWR

## Slide 20: No Tuning Screws
Can’t make it better than you can measure
Can make it worse
Work to known good dimensions
Measure RL to check for problems
  RL > 15 dB = good to go
  RL < 10 dB = fix
Goal = good enough

## Slide 21: VNA – accurate measurement
Calibration routine minimizes Directivity error
  Short
  Open
  Load
TinyVNA only good to 6 GHz
10 GHz+ VNA
  Big, Heavy, and Expensive
  Big, Heavy, and Old

## Slide 22: WAVEGUIDE
VNA needs good Waveguide Calibration
Waveguide Cal kits rare
Waveguide Cal routine?
Coax transitions are a problem

## Slide 23: Waveguide Directional Coupler
Broadside Waveguide Coupler
Very High Directivity
HP tested for 40 dB min Directivity

## Slide 24: Sensitive Detector Required
Coupled reflected power down by:
  Coupling factor -- 10 to 30 dB
  + Return Loss – up to 40 dB
= at least 50 dB below forward power
  -50 dBm small signal
  Test at high power?
Spectrum Analyzer
  TinySA Ultra not that sensitive at 10 GHz
  Big and heavy
  Single frequency measurement

## Slide 25: VNA as detector
Measure S21 with Port 2 at coupled port
No Calibration - Rely on coupler directivity
Measure WG short, then load (antenna)
Difference is Return Loss

## Slide 26: Swept Return Loss
Waveguide Slot Antennas

## Slide 27: 24 GHz with VNA

## Slide 28: Cross-guide Couplers

## Slide 29: Cross-guide Couplers
Crossed Waveguides
Directivity typically 20-25 dB
High coupling factor ≥ -30 dB
Better for power monitor & measurement

## Slide 30: Summary
Accurate microwave measurement difficult
Give it your best shot
Goal = good enough
Get it on the air

## Slide 31: Or screw around

## Slide 32: Lower Frequencies
Directivity ??
Diode detector -beware of harmonics

## Slide 33: A Classic
Precision instrument!
Adjust that Antenna Tuna
To 1.000:1
Diode detector
Are other Amateur meters much better?

## Slide 35: www.w1ghz.org