## Slide 1: Six Meter Rover Antennas
W3CMP 04/2026
Legal Considerations
Physical and Electrical
Limitations
General Categories
New Ideas

## Slide 2: Legal Considerations
Maximum Height for Vehicles - No Federal Limit. Height Set By States. In most states (Eastern U.S.) maximum height is 13.5 feet (162”)
Maximum width for Vehicles - 102” set by Federal Government
Maximum Single Vehicle Length - 40 feet including load
Projecting Load - regulated by states

## Slide 3: Height (Typical) and Width Limits

## Slide 4: Projecting Loads – Overhanging Antennas
PA Vehicle Code § 4924
Front Overhang: Maximum 3 feet beyond the front bumper.
Rear Overhang: Maximum 6 feet beyond the rear of the bed or body.
Flagging/Lighting: A red flag/cloth (12 inches square) is required at the extreme end of the load if it extends
4 feet or more beyond the rear.
Nighttime Requirements: If traveling during hours of darkness, a red light (visible from 500 feet) must be
displayed at the end of the load instead of a flag.
Check Your Own State or States You Will Operate In

## Slide 5: EXCESSIVE REAR OVERHANG
Yagis appear to be DS&E Rover
Specials – 8’ long
No red flag

## Slide 6: Overall Length Violation
Didn’t Get The Memo
12 Element 144 MHz Yagi 7 Element 50 MHz Yagi

## Slide 7: Six Meter Electrical Considerations
Wavelength at 50 MHz = 239+ inches
½ WL ≈ 119 ½”
5/8 WL - Common Stacking Distance for Omnis = 150”
Element lengths of 50 MHz Yagis > legal width of vehicle
Antenna turning radius limits boom length

## Slide 8: Six Meter Antenna Height Propagation Characteristics

## Slide 9: Practical/Physical Considerations
Road To Fire Tower Site In PA
W1RT Rover Mohawk Mtn. CT – K1RA

## Slide 10: Operational Hazards
Bridge near Boston

## Slide 11: Guaranteed Prosecution If Hit

## Slide 12: Six Meter Antennas – Choices For Rovers
If the rover is an entirely mobile, run and gun operation, all street-legal 50MHz antennas are a compromise. If the rover involves stationary, stop and shoot hilltop operation, the mobile limitations may not apply.
Either way, weight and durability should be the biggest considerations. Highway speeds can reach hurricane force winds. For hilltop operation, ease and speed of setup and take down are paramount.

## Slide 13: Gain of Six Meter Antennas – Some Suitable For Rovers

## Slide 14: Omni Directional Six Meter Antennas
Generally some form of bent dipole -
circular or square
Hi-Par Saturn Six, Par Omni OA-50
Cushcraft Loop, Squalo, M2 HO-Loop
Turnstile?
CB 5/8 WL Vertical usable
Original Six Meter Halo W1MUX

## Slide 15: Six Meter Omni Antennas
Advantages
  Easiest and Simplest to Use
  Receive and transmit in all directions – no rotor needed
  Do not exceed width limit on vehicle
Disadvantages
  Receive and transmit in all directions - gain < dipole
  Stacking Distance at 50 MHz = 12 ½ feet

## Slide 16: Typical Six Meter Halo Antennas
Early Halo Ad – Note Price
Cushcraft? Wheel – HamCation 2025

## Slide 17: Common Non- Circular Six Meter Omni Antennas
Par Omni OA-50
M2 HO-Loop

## Slide 18: Homebrew 50MHz Squalo Antennas
W9SR Aluminum Folding Chair Six Meter Loop - January 2002 QST
W3DHJ Version

## Slide 19: Raw materials For Six Meter Squalos
Ready to Cut
Endless Supply

## Slide 20: Gain of Squalo
Squalo gain = 1.21
dBi = -.9 dBd
W9SR

## Slide 21: Six Meter Frankentenna
Ebay Seller – FreqTester
Smaller Than Squalo
Pattern?

## Slide 22: Big Wheel – Too Big
Works well on 144 MHz and 432 MHz
Gain ≈ 5 dBi
Approximate 12’ diameter too big for mobile/rover use
Available from Wimo and
DXEngineering

## Slide 23: Directional Six Meter Rover Antennas
Yagi
KY5ND/R
Moxon

## Slide 24: Yagi
Advantages
Directional
Most Gain 7 – 9 dBi (5 – 7dBd)
Works Well For Fixed Rover
Cheap if CC parts lying around
Many designs to play with
Drawbacks
Size – element lengths exceed
maximum vehicle widths – must
be mounted transversely
Requires Rotator
Assembly often required
Can’t be used effectively while
in motion

## Slide 25: 50 MHz Rover Yagis
K8GP/R June 2016 VHF Contest
50 MHz Yagi Strapped To Van
Andy K1RA Terry W8ZN
Omni Antenna For 50 MHz Operation While Moving

## Slide 26: Three Element Rover Yagi Design
K9MU 3 Element Yagi – 89” Boom
Pattern

## Slide 27: Four Element Rover Yagi Design
K9MU 4 Element Yagi 97” Boom
Element Positions
Pattern and CC Element Taper

## Slide 28: Six Meter Yagis In The Field Stop and Shoot
KG9OV/R
N3IDR/R Blue Knob PA FN00
Elevation 3040’

## Slide 29: Moxon
Advantages
Most Popular Rover Directional Antenna
Broad Front Pattern 75 – 80°
Good Gain 6.1dBi (4 dBd)
Excellent F/B 20 – 25 dB
Element lengths ≈ 85” – do not exceed legal vehicle width
Lower gain than 3 element yagi
Requires rotator
Lightweight
Drawbacks
Lower gain than 3 element yagi
Requires rotator
Not Many Manufacturers – Roll
your Own – programs on internet,
QST April 2004
Commercial antennas –
Par Omni SM-50,
RF-Dxing (India) RFD-MX6
EAntenna – 6MOX DXEngineering

## Slide 30: Moxon
Moxon Configuration
Moxon Pattern Plot DK7ZB

## Slide 31: Six Meter Moxons In Field – Still A Large Antenna
KE4WMF/R
N3UW/R with K1RA

## Slide 32: Six Meter Rover Antennas - New Ideas
Super Moxon - GW4YDX
Moxy - K1BUK

## Slide 33: Super Moxon Information
Invented by Roger Stone
GW3YDX (SK)
Described in July 2010 Radcom (UK)
Designed for 6, 4, and 2 meters
Four bent elements on single boom
76” Boom (1861 mm element length to
tubing centers)
Longest Element Length (A) 85”
allows antenna to be mounted in line
with vehicle and other antennas
Highest Gain for boom length - 8.82 dBi

## Slide 34: Super Moxon Pattern vs. Moxon
Radcom(UK) July 2010

## Slide 35: Moxy
Invented by Dave Ahlgren K1BUK
Half Moxon, Half Yagi
Described in May 2019 QST and
March 2026 QST
Designs for 3 - 6 element antennas
Can be mounted in line with other antennas

## Slide 36: Pattern For 3 element Moxy
Red= Horizontal Plane
Blue = Vertical Plane
Gain 7.15 dBi, F/B 31 dB
2019 four element antenna was designed for 50.2 MHz as compromise between SSB/CW and FT8 uses. 2026 antennas were designed for 50.3 MHz. The 2026 three element design works well from 50 - 51 MHz without perceptible difference in performance.
To center on 50.125 MHz scale by 1.00375
K1BUK March 2026

## Slide 37: Other Ideas - Shrunken Moxon
Designed by Jon Platt W0ZQ
Described in 48th Proceedings of the
Central States VHF Society
Proceedings
Modified MFJ 1896 Moxon
Element lengths reduced to
approximately 60”; boom length
unaltered
Preliminary work not completed
EZNEC files available
W0ZQ

## Slide 38: On six meter rover antennas:
“When the band is open, it doesn’t matter what antenna you use. When the band is closed, it doesn’t matter either.”
                Jack Nyiri AB4CR/R