## Slide 1: An Approach to 5.7,10, 24, 47GHz Q65 mode Beacons
NEWS VHF CONFERENCE 2026
Tom WA1MBA
Paul W1GHZ

## Slide 2
20 Meter CW QSO while on Jet Blue Flight 2066
WA1MBA (MA)
WA1VEI (FL)
14.057 559 529
APR 20, 2026
11:29 Z

## Slide 3: 5.7 thru 47 GHz Q65 Beacons
Original Intent – 47 GHz Beacon to show activity on the band
Has become: Make a simple and cheap beacon board
Get Morse and Q65 Modes on Microwave bands
Build from existing proven designs
Obtain good LO and Image rejection

## Slide 4: Original Intent: 47 GHz Beacon
Several years ago, the 47 GHz band was under attack “Not being used by hams”
We met at the VHF Conference and agreed that beacons would demonstrate amateur activity
WA1MBA developed a 47 GHz quadrupler for beacon use
  Could also be used as bench multiplier and LO source.

## Slide 5: Problem - Simple & Cheap Q65 5-to-47 GHz Beacons
Want a weak signal format for beacons on 5, 10, 24 and 47 GHz “below the noise”
  Straightforward to make a CW beacon
  Good weak signal modulation = Q65 variants
Method: generate signal at 5, 8 – 12 GHz range that has Q65 (plus morse) modulation, and Multiply* to final band
  Be a bit careful of excess Phase Noise, out-of-band leakage
  Must be reproducible
  * Don’t need subsequent multiplier to get 5 and 10 GHz

## Slide 6: Learn (use) what others have done

## Slide 7: Architecture and Solutions
The RFZero™ Arduino synthesizer is affordable (US$80), GPS frequency locked & can make carrier, morse, and digital modes incl Q65 variants at VHF frequencies up to 300 MHz
  Learned from Jim KM5PO - USE THE RFZERO AS A BEACON IF
Needed to design and test a single circuit board that does mixing of the Q65 IF with an LO to produce a 5, or 8 to 12 GHz Signal for direct use on 5 of 10 GHz or further multiplication for 24 or 47 GHz Beacon – Started with the W1GHZ 10 GHz Xvrtr Board
Use Multipliers as needed to get from LO+IF to Final Band
  Example: The WA1MBA Quadrupler can multiply +4dBm signals in the 11.7 GHz range up to the 47 GHz band with 20 mW output power (US$400)
Sector Horn is available - W1GHZ
  Covers 24 and 47 GHz, Use other standard beacon antennas for 5 and 10 GHz (Slots)

## Slide 8: Beacon Examples
RFZero
GPS
145
MHz +
Harm
435 MHz
BPF
435
MHz
7 - 12 GHz
Synthesizer LO
10 MHz Ref
X 4
Multiplier
Horn
47.088
GHz
11.772
GHz
Mixer
11.337
GHz
GPS
LO | RF | MULTIPLIER | BEACON
9.993.200 | 10.368.200 | 1 | 10.368.200
7.629.060 | 8.064.060 | 3 | 24.192.180
11.661.090 | 12.096.090 | 2 | 24.192.180
11.337.090 | 11.772.090 | 4 | 47.088.360
Circuit Board
L
I
L
R

## Slide 9: RFZero™ specialized Arduino PCB
https://rfzero.net/
Excellent website, loads of
accessories, components,
software downloads, advice,
and a “.io” community

## Slide 10: Selecting the Frequency and Multiple for the RFZero™ software
RFZero™ program asks for final frequency and multiplication factor.
  I want a high IF for easier filtering of LO and image, so I chose 435 MHz which can be easily and cheaply filtered. That will effectively be multiplied by 4x in the quadrupler. So, I told the software I wanted 1,740 MHz final frequency
For the multiplier I could state “16” and get 108.75 and therefore would use the 4th harmonic of the fundamental.
But odd harmonics are stronger, so select x12 and it will generate a 145 MHz fundamental and the 3rd harmonic is strong at 435 MHz
It divides the frequency spread of the Q65 signal by the multiplier so that the final RF has the right tone spacing

## Slide 11: RFZero ™ Odd Harmonics Stronger than even

## Slide 12: Noise – example – 47 GHz Beacon
Phase plus Amplitude noise from RFZero™ at 100 MHz is shown to range from -70dBc close in to -75 dBc at 10 kHz.
  When multiplied x12 (take 3rd harmonic and the quadrupler does x4) we would expect a 22 dB increase to the -48dBc to -53dBc range
The Kuhne LO at 11.7 GHz exhibits -72dBc close in to -90 at 10 kHz
  When multiplied by x4 (the Quadrupler)this increases by 12 dB to -60dBc to -78 dBc range
The final beacon signal contains noise dominated by the RFZero phase+amplitude noise of -48 dBc in close to -53 dBc at 10 kHz
These are just estimates. (YMMV)

## Slide 13: Prototype 47GHz Q65 Beacon Without 11.7 GHz filter
Constructed by Jim KM5PO
Uses spare amplifiers I had on hand (no RF filters)
Tested and got good decodes at 47 GHz
RFZero
435 BPF
Kuhne
8-13 LO
Synth
IF Booster
Mixer
11 GHz Amps
(2x 10 GHz LNAs)
Quadrupler
Horn

## Slide 14: Evolution Simplify by putting things on one board
To simplify construction and reproduce, wanted to put separate items on one board
Inexpensive 433 MHz 10 MHz wide connectorized BPF available on-line for about $13 for filtering out unwanted harmonics from the RFZero IF signal
So, put mixer, LO booster amplifier, and 11.7 GHz amplifier/filter chain on one board
W1GHZ makes 10 GHz Personal Beacon and Simple 10 GHz Transverter boards (amplified filters)

## Slide 15: Evolution 11.7 GHz Filter
Pipe Cap Filters (like most filters) may be designed to trade-off bandwidth for insertion loss – wire probe length does it
Affordable PCB material is lossy at 11.7 GHz, so gain is needed to overcome both that loss and filter insertion loss
Sharp filtering is needed to reduce LO and Image frequencies as those will lie in non-amateur EHF bands

## Slide 16: Evolution Simplify extra circuits to One Board
After several experiments settled on a modification of W1GHZ “Simple 10 GHz Transverter” board by connecting 3 pipe-cap filters and 5 amplifier stages for 11.772 GHz
One amplifier stage was replaced with a MAR3+ for 435 MHz IF booster
Mixer in Transverter board is in spec
Modified board is “quite messy” but worked perfectly

## Slide 17: Evolution 1st attempt Hack W1GHZ 10 GHz Transverter PCB
Coax lines added to make IF Booster and 3 pipe-caps,
5 amplifier 11.7 GHz Filter
Used the remaining amplifier stage to boost IF with MAR3+
Bottom and Top of modified “Simple and Cheap10 GHz Xvtr Board”

## Slide 18: Evolution Filter Prototype Performance

## Slide 19: “Frigging Stupid Pipe Caps Can’t live with’em and can’t live without’em”*
PIPE CAPS | OTHER SOLUTION
COST $1, Several Hours first time | COST $ 1,000, No effort
Visual – Eh, who’s looking? | Looks Great, but hidden
Performance Quite acceptable if put in series with amplifier stages | Performance Great in one unit
Tuning – Pretty easy, and adjustable across wide range | Tuning – usually limited
Satisfaction – Built it myself | Satisfaction – Bought it myself
* Quote from WA1MBA

## Slide 20: Better result if you make a Jig for Soldering Pipe Caps to Board (thanks Don W1FKF)

## Slide 21: Adjusting and Reproducing Pipe-Cap Probe Lengths
Working in the Blind
makes it difficult to
get probe lengths right

## Slide 22
LOOK KEMOSABE,
THERE IN THE DIRT
A GOLDEN PIN

## Slide 23: Pins for Pipe-cap Filter Probes Precise Length, Mouser & Digikey

## Slide 24: Tuning is pretty straight-forward Easiest if you have a sweeper

## Slide 25: 10 GHz Pipe-Cap Filter with Pins

## Slide 26: 12 GHz Pipe-Cap Filter with Pins 24 & 47 GHz

## Slide 27: Pipe-Cap Filter Note
What about pipe-cap filter loss?
Some loss is good
Loss between amplifier stages reduces interaction between pipe-caps
  Smoother tuning
  Improved stability
Say it Loud, Say it Clear
“Gain is cheap”

## Slide 28: Phase Noise - Advice
All synthesizers have phase noise
Reduce phase noise by frequency selection
Pick an LO frequency that uses integer-N PLL
Set beacon frequency with RFZero™ IF
No reason IF frequency must be in ham band, but need to filter out unwanted harmonics
Want to choose IF so that subsequent mixing components LO and Image can be sufficiently rejected by pipe-cap filters – higher IF is better

## Slide 29: First trial PCB re-design for Beacon Project
LO INPUT
MIXER
IF
INPUT
RF
OUTPUT
IF
BOOST
RF
FILTER
& AMP
SECTION

## Slide 30: First Trial PCB
Five amplifier stages
Test = Too much gain
Excess LO and Image leakage
Excessive cost with 5 amplifier stages
Redesign with Four amplifier stages for Version 2

## Slide 31: QBEACON CIRCUIT BOARD V2 Simpler and Cheaper
Up-Converter for 5,10 GHz + Microwave Beacons
(add multiplier for 24 & 47)
IF Amplifier, Mixer, 4 RF Amplifiers, 3 Pipe-Cap Filters
External: LO 5 -13 GHz at +7 dBm, 435 MHz IF at -12dBm
RF Out at +7dBm Requires: 8VDC at 250 mA

## Slide 33: Enclosure Increases LO Leakage Standard size aluminum box from Amazon. LO couples from input to output, RF Absorber reduces it
Glued ferrite loaded silicone rubber to enclosure walls
Tested each experiment for LO Leakage

## Slide 34: Evolution of Absorber use to reduce LO Leakage in RF output

## Slide 35: V2 PC board in Enclosure
Inexpensive
Extruded aluminum enclosure from Amazon
Single Piece of
TOJOIN 2mm
Absorber reduces
LO and Image Leakage

## Slide 36: Remember Jim’s Q65 beacon board without a filter?

## Slide 37: KM5PO V2 47 GHz Beacon with QBEACON board

## Slide 38: Board in Enclosure, Operating
8 VDC
RF OUT
LO IN
IF IN

## Slide 39: V2 Performance in Enclosure

## Slide 40: Hacked Xvrt Board vs. V2 Board On 47 GHz

## Slide 42: 47 GHz WA1MBA Quadrupler with W1GHZ Sectoral Horn

## Slide 43: Horn Antenna Beamwidth
Large Aperture gives Narrow Beam
Small Aperture gives Wide Beam

## Slide 44: 47 GHz Sectoral Horn E = 0.56 H = 7.2

## Slide 45: 47 GHz Sectoral Horn E = 0.56 H = 7.2
BEAMWIDTH
3 dB ~ 60°
10 dB ~ 100°

## Slide 46: 47 GHz Sectoral Horn
0.56 = 0.140 inches
WR-28 waveguide height = 0.140 inches
No height taper – easier machining
WR-28 waveguide works at 47 and 24 GHz

## Slide 47: 47 GHz Sectoral Horn at 24 GHz

## Slide 48: 47 GHz Sectoral Horn at 24 GHz
BEAMWIDTH
3 dB ~ 90°
10 dB ~ 200°

## Slide 49: Production Sectoral Horns for 47 or 24 GHz WR-28 Waveguide for both

## Slide 50: Waveguide Adapters for WR-24 and WR-22

## Slide 51: Which Q65 Mode to use on Microwaves?
MODE IS
T/R(S)- A|B|C|D|E|F
e.g. 30-C, 120-B
Wider Tone Spacing allows for more signal spreading like perhaps with rain scatter
Shorter Time makes quicker QSOs
Longer Time has better sensitivity (signal below the noise)
SECS | A | B | C | D | E | F
15 | 6.67 | 13.33 | 26.67 |  |  | 
30 | 3.33 | 6.67 | 13.33 | 26.67 |  | 
60 | 1.667 | 3.33 | 6.67 | 13.33 | 26.67 | 
120 | .75 | 1.5 | 3 | 6 | 12 | 24
300 | .289 | .58 | 1.16 | 2.31 | 4.67 | 9.34
TONE SPACING IN HERTZ

## Slide 52: Which Q65 Mode best for Microwave Beacons?
NTMS
  For Tropo QSO’s 30-A and 15-A. Reason = Quick QSO
  For Beacons 60-C, the same as is used for 1296 EME Reason = Longer Integration Time for S/N and some tone spread for doppler/multipath scatter smearing
NEWS
  W1FKF built 2x 10GHz Beacons with 30-D
  Although 60-C has 3 dB better s/n, much of the beacon cycles are spent in digital while continuous tone and morse are also valuable
  The 10GHz EME beacon is on 60-E
You
  Whatever your choice, post it, including the WZ1V Beacon list

## Slide 53: Summary
Q65 Beacons for 5, 10, 24, and 47 GHz
RF Zero (IF source) $80 assembled
Qbeacon PC Board – Simple and cheap
Add Synthesizer LO *
Add Multiplier for 24 and 47 GHz
10 & 5.7 GHz Beacon (add amplifier)
Inexpensive Beacon
*can use cheaper 3-4 GHz synth and W1GHZ Personal Beacon board to multiply up to desired 10-12 GHz LO range

## Slide 54: At 47 GHz

## Slide 55: Where to get
WA1MBA can supply a few options:
  Bare Boards
  Kits (with instructions)
    Including hard to find NLB310 MMICS
    Can include prepared pipe caps
    Can solder pipe caps onto boards
  Built / tuned to your frequency
  Paired with 47 GHz Multiplier
W1GHZ can supply
  24 & 47 GHz Sector Horn (same horn)
  Adapter to WR22/19 for 47, to WR42 for 24
You must supply
  LO, 8V Power, Enclosure, control, etc

## Slide 56
www.w1ghz.org
www.wa1mba.org

## Slide 57
QUESTIONS?